CAN COM 10-06

September 2001: English

UIT - Secteur de la normalisation des télécommunications

ITU - Telecommunication Standardization Sector

UIT - Sector de Normalización de las Telecomunicaciones

Commission d'études	)							Contribution tardive	)

Study Group				) 10						Delayed Contribution	)  D.@@

Comisión de Estudio	)							Contribución tardia	)

Geneva, 6 September - 14 September 2001

Texte disponible seulement en  )

Text available only in                )  E

Texto disponible solamente en  )

________________________________

Question:	12/10

Source*:	CANADA

Title:	Draft Specification of the Use Case Map Notation (Z.152)

_________________________

ABSTRACT

The attached document entitled, Draft Recommendation Z.152: Languages for Telecommunication Applications - Use Case Map Notation, is the second draft specification of the User Requirements Notation, Functional Requirements (URN-FR). As suggested in the Ottawa SG 10 meeting (April 2001), this document has been split from the original Z.URN contribution (November 2000). The Use Case Map (UCM) notation, which meets a number of criteria for the required notation specified in the definition of URN, is proposed as the notation for URN-FR. This document specifies the UCM language, which now includes a simple path data model for scenario definitions.

PROPOSAL

It is proposed that the attached document be used as a base document for Question 12.

__________________________________________________________________________________________________

* Contact: - Don Cameron,							Tel:	+1 613 763-4486

Nortel Networks 										Fax:	+1 613 763-8080

e-mail:   dcameron@nortelnetworks.com

|  | TELECOMMUNICATION UNION TELECOMMUNICATION COM 10-@@-E STANDARDIZATION SECTOR September 2001 Original: English STUDY PERIOD 2001-2004 |
| --- | --- |

STUDY GROUP 10 - CONTRIBUTION @@

SOURCE *:    	RAPPORTEUR, QUESTION 12/10

TITLE:			DRAFT RECOMMENDATION Z.152: LANGUAGES FOR TELECOMMUNICATION APPLICATIONS — URN-FR: USE CASE MAP NOTATION

_________________________

This document contains the specification of the Use Case Map (UCM) notation, the proposed functional requirements notation (URN-FR) for the draft Recommendation Z.150: User Requirements Notation.

____________________________________________________________________

* Contact: - Don Cameron,							Tel:	+1 613 763 4486

Nortel Networks Corporation					Fax:	+1 613 763 8080

e-mail: 	dcameron@nortelnetworks.com

NEW RECOMMENDATION Z.152: LANGUAGES FOR TELECOMMUNICATIONS APPLICATIONS —
URN-FR: USE CASE MAPS NOTATION

Summary

Scope-objective

This Recommendation defines the UCM (Use Case Map) notation, intended for describing user (functional) requirements scenarios in a formal way without any reference to implementation mechanisms and with optional dependency on component specification. Such a notation is needed to capture user requirements prior to any design. The UCM notation is part of the more general User Requirements Notation (URN).

Coverage

The UCM notation has concepts for the specification of behaviour and structures. This document presents textual and graphical representations of UCM constructs, and an assessment of conformity of the current UCM representations to the requirements for URN.

Applications

UCM is applicable within standard bodies and industry. The main applications areas include telecommunication systems but URN is generally suitable for describing reactive and distributed systems. The range of application is from requirement description to high-level design.

Status/Stability

This proposed Recommendation is a draft reference manual.

The main text is accompanied by the following:

- Annex A			UCM Document Type Definition

- Annex B			Use Case Maps Tutorial

- Appendix I		Tool issues

- Bibliography

- UCM Change Request Form

Associated work

This work is associated with the general URN framework (Z.150), the non-functional requirements language for URN (Z.151: Goal-oriented Requirement Language — GRL), and relations with other SG 10 languages (Z.153).

Keywords

Formal description technique, functional requirements specification, graphical notation, hierarchical decomposition, scenario definitions, specification technique.

FOREWORD

ITU (International Telecommunication Union) is the United Nations Specialized Agency in the field of telecommunications. The ITU Telecommunication Standardization Sector (ITU-T) is a permanent organ of the ITU. The ITU-T is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to standardizing telecommunications on a worldwide basis.

The World Telecommunication Standardization Assembly (WTSA) meets every four years to establish the topics for study by the ITU-T Study Groups, which produce Recommendations on these topics.

The approval of Recommendations by the Members of the ITU-T is covered by the procedure laid down in WTSA Resolution No. 1.

In some areas of information technology, which fall within ITU-T’s purview, the necessary standards are prepared on a collaborative basis with ISO and IEC.

NOTE

In this Recommendation the term recognized operating agency (ROA) includes any individual, company, corporation or governmental organization that operates a public correspondence service. The terms Administration, ROA and public correspondence are defined in the Constitution of the ITU (Geneva, 1992).

INTELLECTUAL PROPERTY RIGHTS

The ITU draws attention to the possibility that the practice or implementation of this Recommendation may involve the use of a claimed Intellectual Property Right. The ITU takes no position concerning the evidence, validity or applicability of claimed Intellectual Property Rights, whether asserted by ITU members or others outside of the Recommendation development process.

As of the date of approval of this Recommendation, the ITU had/had not received notice of intellectual property, protected by patents, which may be required to implement this Recommendation. However, implementers are cautioned that this may not represent the latest information and are therefore strongly urged to consult the TSB patent database.

  ITU   2001

All rights reserved. No part of this publication may be reproduced or utilized in any form or by any means, electronic or mechanical, including photocopying and microfilm, without permission in writing from the ITU.

TABLE OF CONTENTS

1	Introduction	1

2	References	1

3	Definitions	1

4	Abbreviations and acronyms	2

5	Language definition conventions	2

5.1	Graphical representation	2

5.2	Textual  representation	2

6	Use Case Map notation definition overview	2

6.1	Behavioural specification	3

6.2	Scalable system specification	3

6.3	Modular system specification	4

6.4	Valid paths	4

6.5	Architecture	4

6.6	Performance annotations	4

6.7	Functional goals	4

7	Top-level elements	4

7.1.1	XML definition	5

7.1.2	Graphical notation	5

8	Path notation	5

8.1	Hypergraph	5

8.1.1	XML definition	6

8.1.2	Graphical notation	6

8.1.3	Example	6

8.2	Start points	7

8.2.1	XML definition	8

8.2.2	Graphical notation	8

8.3	End points	8

8.3.1	XML definition	8

8.3.2	Graphical notation	8

8.4	Events and conditions	8

8.4.1	XML definition	9

8.4.2	Graphical notation	9

8.5	Responsibility references	9

8.5.1	XML definition	9

8.5.2	Graphical notation	9

8.6	OR-forks and OR-joins	9

8.6.1	XML definition	10

8.6.2	Graphical notation	10

8.7	AND-forks, AND-joins, and synchronizations	10

8.7.1	XML definition	10

8.7.2	Graphical notation	10

8.8	Loops	11

8.8.1	XML definition	11

8.8.2	Graphical notation	11

8.9	Stubs	11

8.9.1	XML definition	12

8.9.2	Graphical notation	12

8.10	Waiting places and timers	12

8.10.1	XML definition	13

8.10.2	Graphical notation	13

8.11	Aborts	13

8.11.1	XML definition	13

8.11.2	Graphical notation	13

8.12	Connections	14

8.12.1	XML definition	14

8.12.2	Graphical notation	14

8.12.3	Examples	14

8.13	Performance and goal annotations	14

8.14	Empty segments	15

8.14.1	XML definition	15

8.14.2	Graphical notation	15

8.15	Path branching specification	15

8.15.1	XML definition	16

8.15.2	Graphical notation	16

9	Components and structures	16

9.1	Component definitions	16

9.1.1	XML definition	17

9.1.2	Graphical notation	17

9.2	Structure specification	18

9.2.1	XML definition	19

9.2.2	Graphical notation	19

9.2.3	Example	19

10	Binding of plug-ins	20

10.1	Plug-in bindings	20

10.1.1	XML definition	21

10.1.2	Graphical notation	21

10.2	Enforced bindings	21

10.2.1	XML definition	21

10.2.2	Graphical notation	21

10.2.3	Example	22

11	Responsibility definitions and dynamic responsibilities	22

11.1.1	XML definition	23

11.1.2	Graphical notation	23

11.1.3	Examples	23

12	Annotations	24

12.1	Performance requirements	24

12.1.1	XML definition	25

12.1.2	Graphical notation	26

12.2	Functional goals	26

12.2.1	XML definition	27

12.2.2	Graphical notation	27

13	Scenario Definitions	27

13.1	Path variables	27

13.1.1	XML definition	27

13.1.2	Graphical notation	27

13.2	Scenarios and groups	28

13.2.1	XML definition	28

13.2.2	Graphical notation	28

14	Static semantic constraints and well-formedness rules	28

14.1	References to identifiers	28

14.2	Well-formed rules for hypergraphs	30

15	Dynamic semantics	30

16	Compliance statement	30

Annex A UCM Document Type Definition	33

Annex B Use Case Maps Tutorial	40

B.1.1	Description of a simplified call screening scenario	40

B.1.2	Evaluation of architectural alternatives for functional entities	41

B.2.1	MSC refinements of bound maps	42

B.2.2	Structural alternatives for functional entities and network entities	43

B.2.3	MSC refinements of bound maps with constrained communication mechanisms	43

B.3.1	Simplified call initiation scenario	44

B.3.2	Three features described in isolation	45

B.3.3	Integrated scenarios	46

B.3.4	Feature interactions and selection policies	47

B.4.1	Description of dynamic architectures	48

B.4.2	Description of mobile behaviour	49

Appendix I Tool issues	51

Bibliography	52

ITU-T Draft Recommendation Z.152

Use Case Map Notation (UCM)

# Introduction

The document defines and illustrates the Use Case Map notation.  It also presents how the UCM notation satisfies the requirements of URN-FR (User Requirements Notation — Functional Requirements), the language describing functional requirements, as defined in Z.150.

# References

The following ITU-T Recommendations and other references contain provisions, which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is published regularly.

ITU-T Q.1200 General Series (1998), Intelligent Networks Recommendation Structure.

ITU-T Z.100 (1999), Specification and Description Language.

ITU-T Z.105 (1999), SDL Combined with ASN.1.

ITU-T Z.109 (1999), SDL combined with UML.

ITU-T, Draft Recommendation Z.110, Guidelines on the Use of Description Techniques

ITU-T Z. 120 (1999), Message Sequence Chart.

ITU-T Z.140 (2001), The tree and tabular combined notation version 3 - TTCN-3: Core language.

ITU-T, Draft Recommendation Z.150, User Requirements Notation

ITU-T, Draft Recommendation Z.151, URN-NFR: Goal-oriented Requirement Language

ITU-T, Draft Recommendation Z.153, URN: Methodological Approach

ITU-T, Draft Recommendation Z.160, Quality Aspects of Protocol-related Recommendations

OMG, Meta Object Facility Specification (MOF), version 1.3.

OMG, XML Metadata Interchange Specification (XMI), version 1.1

OMG - UML RTF, Unified Modeling Language Specification (UML), version 1.4.

W3C Recommendation, Extensible Markup Language (XML) 1.0 (Second Edition).

# Definitions

This Recommendation uses the terms defined in the Definitions section in Z.150 (clause 3).

# Abbreviations and acronyms

This Recommendation uses the abbreviations and acronyms defined in Z.150 (clause 4).

# Language definition conventions

The UCM notation is a graphical notation that supports annotations. Each element of the notation has a textual representation (in XML) and where applicable a graphical representation.

## Graphical representation

Note: The convention used here is informal. At the moment. ITU-T Study Group 17 is in the process of considering a standard for specifying the graphical representation of language elements. Once this standard is available, it will be applied to the UCM notation’s graphical elements.

## Textual  representation

XML (W3C's eXtensible Markup Language) is used for the textual representation of the UCM notation’s elements. The textual representation is contained in a URN-FR Document Type Definition (DTD). XML DTDs describe the syntax of languages in terms of elements and their attributes. Elements define the document structure by describing containment rules, and attributes describe mandatory and optional variables and their data types for further qualifying elements and references to elements. See Appendix I.1 in Z.150 for a brief tutorial on XML.

XML is an appropriate language for describing the integration of the URN-NFR language with the URN-FR language, as well as layout information when necessary. Also, XML supports a simple evolution path towards the integration of URN with UML through technologies such as OMG's Meta-Object Facility (MOF) and XML Metadata Interchange (XMI).

UCM DTD elements and attributes will be described inside shaded boxes using the Courier font. XML elements use lowercase characters (element) whereas XML attributes are in lowercase-italic (attribute) and XML keywords are in uppercase-bold (KEYWORD).

# Use Case Map notation definition overview

The language definition is divided up into a number of sections. The division reflects the major features of the notation.

## Introduction

The URN-FR language specified here is the Use Case Maps (UCM) notation. UCM specifications employ scenario paths to illustrate causal relationships among responsibilities. Furthermore, UCMs provide an integrated view of behaviour and structure by allowing the superimposition of scenario paths on a structure of abstract components. The combination of behaviour and structure enables architectural reasoning after which UCM specifications may be refined into more detailed models such as MSCs and UML interaction diagrams. These detailed models may be transformed into state machines in SDL or UML statechart diagrams and finally into concrete implementations (possibly through automated code generation). Validation, verification, performance analysis, interaction detection, and test generation could be performed at all stages. Thus, the UCM notation enables a seamless transition from the informal to the formal by bridging the modeling gap between requirements (use cases) and design in an explicit and visual way. The UCM notation allows the user to delay the specification of component states and messages and even, if desired, of concrete components to later, more appropriate, stages of the development process. The goal of the UCM notation is to provide the right degree of formality at the right time in the development process.

UCM specifications identify input sources and output sinks as well as describe the required inputs and outputs of a scenario but also integrate many scenarios or related use cases in a map-like diagram. Scenarios can be structured and integrated incrementally. This enables reasoning about and detection of potential undesirable interactions of scenarios and components. Furthermore, the dynamic (run-time) refinement capabilities of the UCM notation allow for the specification of (run-time) policies and for the specification of loosely coupled systems where functionality is decided at runtime through negotiation between components. UCM scenarios can be integrated together, yet individual scenarios are tractable through scenario definitions based on a simple data model.

The UCM notation is a specification language intended for specifiers as well as non-specialists because of its visual, simple, and intuitive nature but at the same time it aims to provide sufficient rigorousness for programmers or tools and contracts.

Most of the characteristics of excellent requirements such as verifiable, complete, consistent, unambiguous, understandable, modifiable, and traceable can be supported by UCMs. Others such as prioritized and annotated are easily incorporated.

UCMs treat scenario paths as first class model entities and therefore build the foundation to more formally facilitate reusability of scenarios and behavioural patterns across a wide range of architectures.

## Behavioural specification

Behavioural specification is accomplished by using the scenario path and responsibility elements of the notation (Sections 8 and 11).

The path notation allows for the specification of an end-to-end path through the system from an input event along a sequence of responsibilities to one of more output events. A path specification can be strictly a behavioural specification. That is, the specification of a path does not require the specification of components. As a result, in UCMs behavioural specifications are first class entities. There is no need to posit an architecture in order to specify the behaviour of the system. Connections between responsibilities are causal; no mechanism is specified or implied.

An input event can belong to a class of events each of which is handled more or less the same by the system. Elements of the path notation allow the specification of the handling of a class of events in one path specification.  The path notation contains numerous control elements such as OR-fork, OR-join, and loop for this purpose.

The path notation also contains elements such as timers, AND-forks (for concurrency within a single path specification), and AND-joins (for synchronization of events internal to a single path specification) required for the specification of reactive system behaviour.

A system response may involve the synchronization of many external input events. Each of these events causes a unique path to execute. In the majority of cases these external events do not belong to the same class and therefore are the subject of separate path specifications. The path notation contains elements such as waiting places and connections to express interactions between these concurrent paths.

## Scalable system specification

The UCM notation has elements to allow it to handle the specification of large systems with complex behaviour. A system specification is essentially a set of path specifications. The constraints on presenting a path specification to a human viewer dictate that a large system specification be composed of a set of root maps. Each root map contains one or more path specifications. A lengthy path specification can fit into a root map by moving segments of it to child maps using the stub-plug-in mechanism. The stub on the parent map represents the plug-in on the child map. A plug-in is a path specification, and it can contain stubs. A child map can, therefore, have children. See Sections  7, 8.9, and 10.

## Modular system specification

The stub-plug-in mechanism may also serve to represent segments of behaviour that recur in many path specifications.

## Valid paths

A path specification may contain many valid paths. The set of valid paths in a path specification is defined by the mechanism of scenario definitions, path variables, and expressions containing path variables. The set of valid paths for a system can be organized into groups and a list of groups. See Section 13.

## Architecture

Architecture is defined by allocating path elements to components. Architectural definition is viewed as a high-level design activity. Developers can use the path specifications created by the requirements engineer as the basis for one or more high level designs. See Section 9.

## Performance annotations

UCMs may be annotated for the purpose of evaluating their performance using performance evaluation tools. See Sections 8.2, 8.13, 8.15 and 12.1

## Functional goals

UCMs may be annotated for the purpose of specifying the functional goals of a path specification. See Sections 8.13 and 12.2.

# Top-level elements

A UCM specification is composed of a collection of (top-level) root-maps and, possibly, of a collection of plug-in-maps, with their bindings. Both root maps and plug-in maps define functional requirements models (ucm-model). Root maps however describe the top-level functional requirements whereas plug-in maps describe (reusable or shared) partial requirements or sub-requirements. A ucm-model contains sub-specifications for its scenario paths and for its component structure. It also has several attributes: an identifier, a name, a title, and a description.

### XML definition

<!ELEMENT urn-fr-spec (root-maps, plug-in-maps?, plug-in-bindings?,

path-variable-list?, scenario-list?)>

<!ELEMENT root-maps (ucm-model)+>

<!ELEMENT plug-in-maps (ucm-model)*>

<!ELEMENT ucm-model (path-spec?, structure-spec?)>

<!ATTLIST ucm-model

ucm-model-id   ID      #REQUIRED

ucm-model-name CDATA   #REQUIRED

title          CDATA   "No title"

description    CDATA   #IMPLIED >

### Graphical notation

No graphical notation is required for these DTD elements.

# Path notation

## Hypergraph

This section defines the UCM path notation used for the definition of causal scenarios (also called maps) included in the element path-spec. A path specification of a ucm-model details the underlying hypergraph that represents the causal scenarios, i.e. the paths. A hypergraph is a graph structure specifying all the elements (called hyperedges) that make up the paths and their interconnections. It also includes the specification of path branching forks as well as constraints on the plug-in maps (i.e. the sub-maps) that can be connected. Hyperedges contain the basic path constructs: start and end points; waiting places; responsibility references; OR-joins and OR-forks; AND-joins and AND-forks (synchronizations); loops; aborts; connections; stubs; performance and goal annotations; and empty segments. All hyperedges have an identifier, a name, a description, and the horizontal/vertical (XY) coordinates of the hyperedge on the map workspace (fx and fy are real numbers between 0 and 1). Attributes lx and ly specify the location of the hyperedge name (if any) relative to the location of the hyperedge (i.e. -fxlx  1-fx, and -fy ly  1-fy).

A hypergraph has a list of connections between hyperedges (hyperedge-connection). Each such connection is a source-hyperedge attribute and a list of references to target hyperedges (hyperedge-ref). These references (of attribute type IDREF) must refer to existing hyperedge identifiers (of attribute type ID).

### XML definition

<!ELEMENT path-spec (hypergraph)?>

<!ELEMENT hypergraph (hyperedge*, hyperedge-connection*,

path-branching-spec*, enforce-bindings*)>

<!ELEMENT hyperedge ( (start | end-point | responsibility-ref |

fork | join | synchronization | loop | stub |

waiting-place | abort | connect | timestamp-point |

goal-tag | empty-segment)) >

<!ATTLIST hyperedge

hyperedge-id     ID      #REQUIRED

hyperedge-name   CDATA   #IMPLIED

fx               NMTOKEN #IMPLIED

fy               NMTOKEN #IMPLIED

lx               NMTOKEN #IMPLIED

ly               NMTOKEN #IMPLIED

description      CDATA   #IMPLIED >

<!ELEMENT hyperedge-connection (hyperedge-ref)*>

<!ATTLIST hyperedge-connection

source-hyperedge IDREF   #REQUIRED >

<!ELEMENT hyperedge-ref EMPTY>

<!ATTLIST hyperedge-ref

hyperedge-id     IDREF   #REQUIRED >

### Graphical notation

A line (spline) is used to represent connected path elements (hyperedges) that belong to a causal scenario. The hyperedges themselves have different visual representations depending on their nature, and they will be defined formally in the next sub-sections.

### Example

The next two figures are used as an introduction example to the path notation. The core elements are present in the simple map shown in Figure 1/Z.152. This causal scenario path represents a simplified call connection initiated through the start point req. The system first checks whether the call should be allowed (responsibility chk) and then verifies whether the called party is busy or idle (vrfy). The assumption in this scenario (i.e. a precondition) is that the called party is idle. Then, the system status is updated (upd) and a resulting ringing event occurs at the end point (ring). The causal path is shown as a line (usually a spline) that connects the various hyperedges.

Basic UCM notation elements

UCMs can also help structuring and integrating scenarios in various ways, e.g. sequentially, as alternatives (with OR-forks/joins) or concurrently (with AND-forks/joins). Conditions can be attached to alternative paths. Stubs are containers for sub-maps called plug-ins and can also be used to integrate, structure, and reuse scenarios. Figure 2/Z.152(a) extends the simple connection example by using some of these notation elements. The verification responsibility (vrfy) may cause the selection of the idle path, which then splits into two concurrent paths for ringing (ring) and for signaling (sig) the occurrence of a prepared ringback reply (prb). Else, the busy path could be selected, which would result in the signaling of a prepared busy reply (pb). Figure 2/Z.152(b) presents a potential plug-in map for the Originating stub from Figure 2/Z.152(a). This TeenLine plug-in checks the current time (chkTime) and, if in the predefined range, requires a valid personal identification number (PIN) to be provided in a timely fashion for the call initiation to continue. If an invalid PIN is provided, or if a time-out occurs, then a denied reply is prepared (pd). The input/output path segments attached to stubs are labeled for binding plug-in start/end points. The binding relationship is {<IN1, in1>, <OUT1, out1>, <OUT2, out2>} connects the stub path segments of the parent map to the start/end points of the plug-in.

Extension of the call connection example and additional UCM notation elements

All these elements are defined individually in the remaining sub-sections.

## Start points

A start point is where scenarios are caused, upon the arrival of associated triggering events and/or the satisfaction of associated preconditions. A start hyperedge should be connected to only one target hyperedge. It has no source hyperedge except when linked to an end-point by a connect hyperedge. A triggering-event-list gives the set of events that can initiate the causal scenario along a path. The required events can be composed in many ways (user-defined), but by default one of them is sufficient for triggering the scenario. The precondition-list must also be satisfied in order for the scenario to be enabled. Several attributes used for performance analysis can be attached to a start point:

mean: parameter for exponential and Erlang arrival distributions.

value: parameter for deterministic arrival distribution.

low, high: parameters for uniform arrival distribution.

kernel: parameter for Erlang arrival distribution.

expert-distribution: parameter for expert arrival distribution (user-defined).

### XML definition

<!ELEMENT start (triggering-event-list?, precondition-list?)?>

<!ATTLIST start

arrival     (exponential | deterministic

| uniform | erlang

| expert | none)          "none"

mean                NMTOKEN            #IMPLIED

value               NMTOKEN            #IMPLIED

low                 NMTOKEN            #IMPLIED

high                NMTOKEN            #IMPLIED

kernel              NMTOKEN            #IMPLIED

expert-distribution CDATA              #IMPLIED >

<!ELEMENT triggering-event-list (event)*>

<!ATTLIST triggering-event-list

composition         CDATA              "OR" >

### Graphical notation

A start point is shown as a filled circle at the beginning of a path, with its hyperedge-name attribute as a label.

## End points

Scenario effects are represented by end points, which describe resulting events and/or post-conditions. An end-point hyperedge should be connected to only one source hyperedge. It has no target hyperedge except when linked to a start or to a waiting-place by a connect hyperedge. A resulting-event-list gives the set of events that result from the completion of the causal scenario path. These events can be composed or selected in many ways (user-defined), but by default all of them are output. The post-condition-list is satisfied once the sequence is completed.

### XML definition

<!ELEMENT end-point (resulting-event-list?, postcondition-list?)?>

<!ELEMENT resulting-event-list (event)*  >

<!ATTLIST resulting-event-list

composition         CDATA              "AND" >

### Graphical notation

An end point is shown as a thick bar with its hyperedge-name attribute as a label.

## Events and conditions

Conditions have a name and a user-defined description. No specific syntax or data language is specified at the moment, although in the future conditions should be described in a language compatible with the data-language attribute of the urn-spec element. Conditions can be grouped as lists of preconditions and post-conditions. These conditions can be composed in a user-defined way, but by default they must all be satisfied ("AND" composition). An event is an element with a name and a description.

### XML definition

<!ELEMENT postcondition-list (condition)*>

<!ATTLIST postcondition-list

composition CDATA   "AND" >

<!ELEMENT precondition-list (condition)*>

<!ATTLIST precondition-list

composition CDATA   "AND" >

<!ELEMENT condition EMPTY>

<!ATTLIST condition

name        NMTOKEN  #REQUIRED

description CDATA    #IMPLIED >

<!ELEMENT event EMPTY>

<!ATTLIST event

name        NMTOKEN  #REQUIRED

description CDATA    #IMPLIED >

### Graphical notation

There is no graphical notation defined for these elements.

## Responsibility references

A responsibility reference refers, through its resp-id attribute, to a responsibility defined in responsibility-definitions. An optional arrow-position attribute indicates the position of the arrow when the responsibility is dynamic (see dynamic-resp in Section 11). The responsibility-ref hyperedge is connected to only one source hyperedge and to one target hyperedge.

### XML definition

<!ELEMENT responsibility-ref EMPTY>

<!ATTLIST responsibility-ref

resp-id        IDREF     #REQUIRED

arrow-position NMTOKEN   #IMPLIED >

### Graphical notation

A responsibility reference is shown as a cross on a path with the resp-name attribute of the referenced responsibility as a label. Responsibilities that are dynamic are shown with arrows, as described in Section 11.

## OR-forks and OR-joins

OR-forks represent on a path where scenarios split as two or more alternative paths. A fork has several target hyperedges and only one source hyperedge. OR-joins capture the merging of two or more independent scenario paths. A join has several source hyperedges and only one target hyperedge. Both elements have an orientation attribute which describes, in degrees (0º for right, 90º for up, etc.), the orientation of the construct. Conditions can be attached to forked paths, as specified in path-branching-spec (Section 8.15).

### XML definition

<!ELEMENT fork EMPTY>

<!ATTLIST fork

orientation NMTOKEN #IMPLIED >

<!ELEMENT join EMPTY>

<!ATTLIST join

orientation NMTOKEN #IMPLIED >

### Graphical notation

An OR-fork is shown as splitting paths (two or more). If specified, the hyperedge-name attribute of this hyperedge is shown as a label.

An OR-join is shown as merging paths (two or more). If specified, the hyperedge-name attribute of this hyperedge is shown as a label.

## AND-forks, AND-joins, and synchronizations

AND-forks represent on a path where scenarios split as two or more concurrent paths (i.e. the concurrency level is increased). AND-joins capture the synchronization of two or more concurrent scenario paths (i.e. the concurrency level is decreased). Both AND-joins and AND-forks are special cases of the synchronization element, which has several source and target hyperedges. An explicit cardinality (1:N, N:1, 2:3, etc.) can also be associated to a synchronization to specify how many instances of the source path need to synchronize and/or how many instances of the target path are created concurrently. This element has an orientation attribute describing its orientation, in degrees (0º for right, 90º for up, etc.).

### XML definition

<!ELEMENT synchronization EMPTY>

<!ATTLIST synchronization

cardinality-source  NMTOKEN #IMPLIED

cardinality-target  NMTOKEN #IMPLIED

orientation         NMTOKEN #IMPLIED >

### Graphical notation

A synchronization is shown as a thin bar, generally perpendicular to the path(s). If specified, the cardinality is shown in the format cardinality-source:cardinality-target. If specified, the hyperedge-name attribute of this hyperedge can also be shown as a label.

The figure above presents examples of AND-forks that have one source path and multiple target paths.

The figure above presents examples of AND-joins that have multiple source paths and one target path.

The figure above presents examples of general synchronizations with multiple source paths and multiple target paths.

## Loops

Loops are captured explicitly by the loop element. It has two source hyperedges, which represent the original path and the end of the looping path. It also has two target hyperedges, which represent the continuation of the original path and the beginning of the looping path. An exit-condition attribute specifies the condition under which the loop is exit (the looping path may even never been entered). The looping path may contain any other hyperedge, including other loops. This element has an orientation attribute which describes its orientation, in degrees (0º for right, 90º for up, etc.).

### XML definition

<!ELEMENT loop EMPTY>

<!ATTLIST loop

orientation    NMTOKEN  #REQUIRED

exit-condition CDATA    #IMPLIED >

### Graphical notation

The loop is shown as a path element with two incoming path segments followed immediately by two outgoing path segments (similar to an OR-join followed by an OR-fork). If specified, the hyperedge-name attribute of this hyperedge is shown as a label. The exit condition can also be shown between square brackets near the exit path.

## Stubs

Stubs are containers for plug-in maps (i.e. sub-maps). Stubs can be of type static or of type dynamic. While static stubs contain only one plug-in, dynamic stubs may contain multiple plug-ins whose selection can be determined at run-time according to a selection-policy. Such a policy can make use of preconditions, assertions, run-time information, composition operators, etc. in order to select the plug-in(s) to use. Selection policies are described with a (formal or informal) language suitable for the context where they are used. The plug-in maps are sub-maps that describe locally how a feature modifies the parent causal paths. Multiple levels of stubs and plug-ins can be used. Stubs that involve negotiations with components other than the one to which the stub is allocated are called shared stubs.

A stub can have several entry points and exit points, connected respectively to source and target hyperedges. The paths segments that are connected to the stub need to be bound to the paths of the plug-ins in order to express continuity. This is done through explicit binding in plug-in-bindings (Section 10.1). Bindings can be enforced to ensure particular path continuity, even in the presence of a plug-in (see enforce-bindings, Section 10.2). stub-entry-list contains identifiers for stub entry points connected to source hyperedges, whereas stub-exit-list contains identifiers for stub exit points connected to target hyperedges.

Stubs may also contain preconditions, post-conditions, and a specification of service requests for performance requirements (Section 12.1).

### XML definition

<!ELEMENT stub (stub-entry-list, stub-exit-list, precondition-list?,

postcondition-list?, service-request-spec?)>

<!ATTLIST stub

type              (static | dynamic)  "static"

shared            (yes | no)          "no"

selection-policy  CDATA               #IMPLIED>

<!ELEMENT stub-entry-list (stub-entry)+>

<!ELEMENT stub-entry EMPTY>

<!ATTLIST stub-entry

stub-entry-id   ID      #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

<!ELEMENT stub-exit-list (stub-exit)+>

<!ELEMENT stub-exit EMPTY>

<!ATTLIST stub-exit

stub-exit-id    ID      #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

### Graphical notation

Stubs are shown as diamonds connecting input path segments to output path segments. The hyperedge-name attribute of this hyperedge is shown as a label. Diamonds for dynamic stubs are drawn with dotted lines.

Shared stubs are shown with two overlapping diamonds, and they can be either static or dynamic.

## Waiting places and timers

A waiting place is an element on a path where the causal flow stops until it is restarted by a specific event coming from the environment or from some other path via a connect element. The triggering-event-list gives the set of events that can restart the causal flow on a path. The precondition-list must be satisfied in order for the flow to restart. A timer is a special waiting place where the flow resumes along the continuation path if the triggering event arrives in a timely fashion, otherwise the flow continues on a timeout path. The wait-type attribute is a user-defined description of the type of waiting (e.g. it could collect the triggering events before the causal flow gets to the waiting place).

A waiting-place has usually one source hyperedge and one target hyperedge. However, it can have two target hyperedges when there is a timeout path (the latter uses an abort hyperedge, see Section 8.11), and more than one source hyperedges when linked to connect hyperedges (Section 8.12).

### XML definition

<!ELEMENT waiting-place (triggering-event-list?, precondition-list?)?>

<!ATTLIST waiting-place

timer           (yes | no)    "no"

wait-type       CDATA       #IMPLIED >

### Graphical notation

Due to their similarity with start points, waiting places are also shown as filled circles, but this time located on a path. The hyperedge-name attribute of this hyperedge is shown as a label.

Timers are shown with a clock symbol. The timeout path that exits from the timer is shown with a broken line, to distinguish it from the initial continuation path.

## Aborts

The abort describes, in an exception-like manner, that one scenario path aborts or disables the flow along another path. It is also used to describe the timeout path exiting from a timer. The abort has one source hyperedge and one target hyperedge, which can be empty segments or stubs. In the case of a timeout path, the source hyperedge is a waiting place (timer) and the target hyperedge is an empty segment.

### XML definition

<!ELEMENT abort EMPTY>

### Graphical notation

The abort is shown as a broken arrow linking an empty point or a stub to an empty point or a stub. The head of the arrow points towards the target hyperedge. When defined, the hyperedge-name attribute of this hyperedge is shown as a label.

When used to represent a timeout path, the abort is shown as a broken line instead of as an arrow (Section 8.10).

## Connections

Connections describe explicit interactions between two different scenario paths. Connections capture synchronous interactions by linking an end point to a start point or to a waiting place (or timer). Such interactions trigger the target start point or waiting place (or timer). This triggering can also be achieved in-passing (without waiting) through asynchronous interactions. In this case, the source hyperedge is an empty segment. The connection has one source hyperedge (end point or empty segment) and one target hyperedge (start point or waiting place).

### XML definition

<!ELEMENT connect EMPTY>

### Graphical notation

A connect hyperedge does not have a graphical representation as an element. It is however shown as the juxtaposition of an end point with a start point of waiting place (for synchronous interactions) or as the juxtaposition of an empty path segment with a start point of waiting place (for asynchronous interactions).

### Examples

The example above shows a synchronous interaction on a waiting place. Responsibility R cannot be performed until the waiting place is triggered by the end point.

The example above shows a synchronous interaction on a start point. Responsibility R cannot be performed until the start point is triggered by the end point.

The example above shows a synchronous interaction on a timer. Responsibility R cannot be performed until the timer is triggered by the end point, in a timely fashion. If the triggering event does not arrive in time, then the timeout path is followed.

The example above shows an asynchronous interaction on a start point. Responsibility R cannot be performed until the start point is triggered in passing by the empty path segment.

## Performance and goal annotations

Specific hyperedges can be use to annotate paths for performance requirements (timestamp-point) or functional goals (goal-tag). These elements have one source hyperedge and one target hyperedge. They are defined with the other elements related to annotations in Section 12.

## Empty segments

An empty segment is used to add characteristics to a path such as the indication of a failure point (where the causal flow could stop for a non-specified reason, which is useful to describe when robustness needs to be modeled), of the direction of the causal flow, or that the responsibilities immediately preceding and following it are shared. Shared responsibilities explicitly imply the existence of a complex communication mechanism (e.g. multiple exchanges of messages satisfying some constraints, protocols, or negotiation rules) used across components.

An empty segment may also specify preconditions for the next hyperedge or post-conditions of the previous hyperedge. An optional path-label can be defined for this element. The empty segment has one source hyperedge (more when linked to an abort) and one target hyperedge (more when linked to a connect).

### XML definition

<!ELEMENT empty-segment (precondition-list?, postcondition-list?)?>

<!ATTLIST empty-segment

path-label      CDATA                      #REQUIRED

characteristics (failure-point | shared

| direction-arrow )       #IMPLIED

show-label      (yes | no)                 "no" >

### Graphical notation

An empty element without any associated attribute does not have any specific graphical representation (the conditions are not shown). This hyperedge however has a position and it can be used to add points along a spline, or to allocate a path segment to a component. In all cases, the path-label attribute can be displayed, according to the show-label policy.

An empty point can be characterised as a failure point, which is then shown with a ground symbol.

As shown with the symbol above, an empty point can be used to indicate that two responsibilities (e.g. R1 and R2, usually bounded to two different components) are shared.

In long or ambiguous paths, an empty point can be used to indicate visually the current direction of the causality flow. The direction is shown with an arrow on the path.

## Path branching specification

A path branching specification contains the characteristics by which the output branches (referenced by the next empty-segment) of an existing OR-fork (referenced by fork-id) are selected at run time. The characteristic may be described with logical conditions or preconditions. The branch-condition is a formalization of this characteristic where the condition attached to a branch is specified using a logical expression composed of Boolean constants (T or F) or variables (defined in 13.1), potentially connected by logical operators: and ‘&’, or ‘+’, not ‘!’, equal ‘=’, not equal ‘!=’, as well as brackets for indicating precedence ‘()’.

A probability (real number between 0 and 1) can also be assigned to the various branches. The sum of all probabilities for a given OR-fork should be equal to 1. Attributes lx and ly specify the location of the characteristic relative to the location of the referenced fork hyperedge (i.e. -fxlx  1-fx, and -fy ly  1-fy).

The path-branching-spec elements are found after the hyperedge elements in a URN-FR description because the former contain references to the latter.

### XML definition

<!ELEMENT path-branching-spec (path-branching-characteristic)*>

<!ATTLIST path-branching-spec

fork-id    IDREF   #REQUIRED >

<!ELEMENT path-branching-characteristic EMPTY>

<!ATTLIST path-branching-characteristic

characteristic   CDATA   #IMPLIED

branch-condition CDATA   #IMPLIED

probability      NMTOKEN #IMPLIED

empty-segment    IDREF   #REQUIRED

lx               NMTOKEN #IMPLIED

ly               NMTOKEN #IMPLIED >

### Graphical notation

Each path branching characteristic is shown in the format [characteristic : probability]. If the characteristics or probabilities are not both defined, then the format can be simplified to [characteristic] or to [:probability].

# Components and structures

The UCM notation combines behavioural scenarios with structures of abstract components. This section defines the component notation and its role in a structure.

## Component definitions

The component-definitions element, found in definitions, describes the structural entities of a UCM specification, i.e. the components. Components represent, at the requirements level, abstract entities corresponding to actors, processes, objects, containers, agents, and so on. All components have a name, a unique identifier, a description, and a colour (in RGB, 24 bits). Other visual attributes could be added to this element.

Components are divided in two different categories: regular components and pools. Regular components can be of various types, which conform to the component-notation attribute found in urn-spec. In Buhr's notation, which is used by default in the UCM language, the component type can be one of the following:

Team: default/generic component, used as a container for sub-components of any type.

Process: active component, which implies the existence a control thread.

Object: passive component, which is usually controlled by a process.

Agent: autonomous component, which act on behalf of other components.

All types of regular components also contain the following boolean attributes:

slot: placeholder for a dynamic component that represents, in a static way, a role that can be populated by actual instances of components at different times.

protected: the execution of causal paths bound to the component is ruled by a mutual exclusion mechanism.

replicated:  multiple instances of this component exist simultaneously. The number of instances can be set using a replication-factor.

An attribute used for performance analysis may optionally be specified:

processor-id: reference to a valid processor on which this component executes.

Slots are containers for dynamic components in execution, whereas pools are containers for dynamic components that are not executing. Pools mainly serve the dynamic self-configuring aspect of functional scenarios. A pool can be attributed an arbitrary component type (process, team, object, agent, etc.) or a list of plug-ins usable in dynamic stubs (see the plug-in-pool element in Section 10.1). Pools can only perform responsibilities that are dynamic, for example, to move components or plug-ins in or out a path (Section 11).

### XML definition

<!ELEMENT component-definitions (component)*>

<!ELEMENT component ((regular | pool))>

<!ATTLIST component

component-id        ID          #REQUIRED

component-name      CDATA       #REQUIRED

description         CDATA       #IMPLIED

colour              NMTOKEN     #IMPLIED >

<!ELEMENT regular EMPTY>

<!ATTLIST regular

type                NMTOKEN     "team"

protected           (yes | no)  "no"

slot                (yes | no)  "no"

replicated          (yes | no)  "no"

replication-factor  NMTOKEN     "1"

processor-id        IDREF       #IMPLIED >

<!ELEMENT pool EMPTY>

<!ATTLIST pool

type                NMTOKEN  #REQUIRED >

### Graphical notation

Component definitions do not have a graphical presentation per se. However, references to these components are shown visually (see Section 9.2). A team is represented with a rectangle, a process with a parallelogram, an object with a rounded-corner rectangle, and an agent as a rectangle with a thick border. The component-name is also displayed on top of the component. If the colour attribute is set, then the component border uses this colour.

The boolean attributes also have a graphical representation. Slot components are shown with a dotted border, protected components with a double-line border, and replicated components as a stack with several instances. All these attributes and their graphical can be used simultaneously.

A pool is shown as a partially filled container.

## Structure specification

The structure specification is part of a ucm-model and contains references to components, which in turn enumerate the responsibilities and other hyperedges allocated to these components. A component-ref element has a unique identifier and a reference to a valid component-id found in component-definitions. It also includes a responsibility-list, which references valid responsibility reference hyperedges, as well as an other-hyperedge-list, which references valid hyperedges (other than responsibility references) found in the hypergraph. All these referenced hyperedges are said to be bound or allocated to the component. Component references possess the horizontal/vertical (XY) coordinates of the component on the map workspace (fx and fy are real numbers between 0 and 1), together with width and height.

Regular components (e.g. teams) may contain sub-components. A sub-component has a component-parent attribute that references the parent component (a valid component-ref-id). Pools are not allowed to contain sub-components.

A component reference is given a user-defined role, which is a characterization of this particular instance. For example, a component named "User" may be involved in two several roles, such as "Initiator" or "Responder".

Finally, a component reference can be declared as anchored. By default, a non-anchored component reference used in a plug-in implies that it is a sub-component of the parent map component where the stub is located. An anchored component reference used in a plug-in is an explicit indication that it is not a sub-component of the parent map component where the stub is located (hence, it must be declared somewhere else in the UCM specification).

### XML definition

<!ELEMENT structure-spec (component-ref)* >

<!ELEMENT component-ref (responsibility-list?, other-hyperedge-list?)?>

<!ATTLIST component-ref

component-ref-id      ID          #REQUIRED

referenced-component  IDREF       #IMPLIED

component-parent      IDREF       #IMPLIED

role                  CDATA       #IMPLIED

fx                    NMTOKEN     #REQUIRED

fy                    NMTOKEN     #REQUIRED

width                 NMTOKEN     #REQUIRED

height                NMTOKEN     #REQUIRED

anchored              (yes | no)  "no"  >

<!ELEMENT responsibility-list (hyperedge-ref)*>

<!ELEMENT other-hyperedge-list (hyperedge-ref)*>

### Graphical notation

Component references use shapes and patterns corresponding to their respective component definitions (Section 9.1). Hyperedge references are allocated to components by superimposing them to component references.

A sub-component is shown as being embedded in its parent component. When non-empty, the role of a component reference is shown in the format component-name:role. Anchored component references are shown with a shadow (e.g. using small oblique lines) under the component.

### Example

Drawing path elements on components is a simple means to evaluate alternative candidate architectures. For instance, the simple call connection scenario (Figure 3/Z.152) can be bound to various component structures.

Basic UCM notation elements

Figure 3/Z.152 shows how the same scenario path can be reused on three different example architectures. The first one (a) is a simplistic solution involving the system and two users (roles A and B). The second architecture (b) splits the responsibilities into two agent instances (roles A and B). The third solution (c) maps the scenario path to a more conventional architecture based on the Intelligent Network model.

# Binding of plug-ins

Plug-in maps are connected by bindings to stubs in parent maps. This section presents this binding mechanism together with additional constraints that can be imposed on stub to ensure path continuity (enforced bindings).

## Plug-in bindings

A plug-in map is a ucm-model that can be substituted to a stub in a parent map. The plug-in-bindings element contains a list of plug-in bindings and a list of plug-in pools.

The binding between a plug-in (referred to by submap-id) and a stub (stub-id) in its parent map (parent-map-id) is defined by input and output connection lists. An in-connection joins a stub entry identifier (stub-entry-id, a reference to a valid stub-entry-id in the stub) with a start hyperedge from the plug-in (valid hyperedge-id). An out-connection joins a stub exit identifier (stub-exit-id, a reference to a valid stub-exit-id in the stub) with an end point from the same plug-in (valid hyperedge-id).

A plug-in can be bound to multiple stubs, which improves the reusability of sub-maps. Start points and end points in a plug-in do not all have to be bound to a stub. Stub entry points and exit points do not all have to be bound either.

The branch-condition is a formalization of the selection policy where the precondition attached to the bound plug-in is specified using the data model. The precondition is a logical expression composed of Boolean constants (T or F) or variables (defined in 13.1), potentially connected by logical operators: and ‘&’, or ‘+’, not ‘!’, equal ‘=’, not equal ‘!=’, as well as brackets for indicating precedence ‘()’.

A plug-in-pool is an identifier container for plug-ins, where plug-ins can be stored or retrieved. The attribute ucm-model-id is a reference to an existing plug-in map identifier whereas pool-id is a reference to a pool component.

### XML definition

<!ELEMENT plug-in-bindings (plug-in-binding*, plug-in-pool*)? >

<!ELEMENT plug-in-binding (in-connection-list?, out-connection-list?)?>

<!ATTLIST plug-in-binding

parent-map-id    IDREF   #REQUIRED

submap-id        IDREF   #REQUIRED

stub-id          IDREF   #REQUIRED

branch-condition CDATA   #IMPLIED>

<!ELEMENT in-connection-list (in-connection)*>

<!ELEMENT in-connection EMPTY>

<!ATTLIST in-connection

stub-entry-id    IDREF   #REQUIRED

hyperedge-id     IDREF   #REQUIRED >

<!ELEMENT out-connection-list (out-connection)*>

<!ELEMENT out-connection EMPTY>

<!ATTLIST out-connection

stub-exit-id     IDREF   #REQUIRED

hyperedge-id     IDREF   #REQUIRED >

<!ELEMENT plug-in-pool EMPTY>

<!ATTLIST plug-in-pool

pool-id          IDREF   #REQUIRED

ucm-model-id     IDREF   #REQUIRED >

### Graphical notation

There is no graphical notation defined for the binding of plug-ins. Pools have a graphical representation described in Section 9.1.

## Enforced bindings

Required bindings can be enforced while defining a stub in order to preserve path continuity in the parent map. Continuity in a path-binding element is expressed as a relation between the entry and exit points of a given stub (i.e. stub-entry-id and stub-exit-id must be valid references according to stub stub-id). Plug-ins whose bindings do not satisfy this constraint will not be selectable.

### XML definition

<!ELEMENT enforce-bindings (path-binding)*>

<!ATTLIST enforce-bindings

stub-id         IDREF   #REQUIRED >

<!ELEMENT path-binding EMPTY>

<!ATTLIST path-binding

stub-entry-id   IDREF   #REQUIRED

stub-exit-id    IDREF   #REQUIRED >

### Graphical notation

There is no graphical notation defined for these elements.

### Example

Assume the enforced binding relationship {<IN1, OUT1>} assigned to Originating stub in Figure 2/Z.152(a). Valid plug-ins are required to provide a path that connects IN1 to OUT1. The plug-in TeenLine in Figure 2/Z.152(b) possesses such a path according to its binding relationship ({<IN1, in1>, <OUT1, out1>, <OUT2, out2>}), hence it is a valid plug-in.

The Default plug-in shown above may or may not satisfy the same enforced binding relationship. The binding relationship {<IN1, defIn1>, <OUT1, defOut1>} is a valid binding of this plug-in (the hyperedge labels are used here to refer to the elements in the relationships, but the relationships are really using identifiers). However, the binding relationship {<IN1, defIn1>, <OUT2, defOut1>} is invalid because is does not enable path continuity between IN1 and OUT1.

# Responsibility definitions and dynamic responsibilities

Responsibilities are processing tasks (e.g. procedures, functions, actions, etc.) that are referenced by scenarios and by components. They are described in the responsibility-definitions element. A responsibility has a name, a description, and a unique identifier that can be referenced by components (in component-ref) and by paths (in the hyperedge responsibility-ref). Preconditions and post-conditions can be associated to a responsibility. A responsibility may also include a sequence of execution statements (exec-sequence) in a user-defined format. Such an execution sequence can be used for fine-grained modeling purpose, e.g. for performance analysis.

Responsibilities can be defined as being dynamic. Dynamic stubs show how behaviour patterns can evolve at run time, whereas dynamic responsibilities and dynamic components show how a structure of components evolves at run time. A dynamic responsibility (dynamic-resp) performs an action on dynamic components or on plug-ins, in or out of a path. The different types of actions are:

create: for dynamic components, creates a new component instance on a path (in) or in a slot or a pool of components (out). For plug-ins, this action creates a new plug-in instance on a path (in) or in a stub or a pool of plug-ins (out).

move: for dynamic components, moves a component instance from a slot or a pool of components to a path (in) or from a path to a slot or a pool (out). For plug-ins, this action moves a plug-in instance from a stub or a pool of plug-ins to a path (in) or from a path to a stub or a pool (out).

move-stay: similar to move, but moves a reference (i.e. an alias) to the component or plug-in while leaving the original instance in place. The same instance hence become visible in several places at once.

copy: similar to move, but moves a distinct copy of to the component or plug-in while leaving the original instance in place. The two copies then evolve separately.

destroy: for dynamic components, deletes a component instance found in a slot or a pool of components (in) or on a path (out). For plug-ins, this action deletes a plug-in instance found in a stub or a pool of plug-ins (in) or on a path (out).

A dynamic responsibility may also be associated to an explicit source pool. The sourcepool attribute is the pool-name of an existing pool in the ucm-model. The relative length of the displayed arrow may also be specified (arrow-length is a real number between 0 and 1).

Responsibilities can also be used for describing performance annotations with the elements data-store-spec and service-request-spec. These elements will be discussed in Section 12

### XML definition

<!ELEMENT responsibility-definitions (responsibility)*>

<!ELEMENT responsibility (data-store-spec?, service-request-spec?,

(precondition-list?, postcondition-list?)?,

dynamic-resp?)?>

<!ATTLIST responsibility

resp-id         ID      #REQUIRED

resp-name       CDATA   #IMPLIED

exec-sequence   CDATA   #IMPLIED

description     CDATA   #IMPLIED >

<!ELEMENT dynamic-resp EMPTY>

<!ATTLIST dynamic-resp

type         (move | move-stay | create

| copy | destroy)         #REQUIRED

direction    (in | out)                  #REQUIRED

sourcepool   CDATA                       #IMPLIED

arrow-length NMTOKEN                     #IMPLIED >

### Graphical notation

Responsibility definitions do not have a graphical presentation per se. However, references to these responsibilities are shown visually. Section 8.5 already presents the graphical notation for references to non-dynamic responsibilities (i.e. a cross on a path).

References to dynamic responsibilities are shown with arrows rather than with crosses. Different types of arrows are used for the five types of actions.

### Examples

Dynamic responsibilities can be used to populate slots with dynamic components. In this example, a dynamic component is moved from a pool of components to the path (movein) and then moved out of the path to occupy a slot (moveout). This component can then perform responsibility R. This pool acts as a repository for inactive components.

The partial scenario shown above presupposes that SlotA is occupied by a dynamic component.  After performing R1, this dynamic component is destroyed (destroyA), but the slot remains in order to be populated again at a later time. Then, a new dynamic component is created in SlotB (createB), which in turn performs R2.

In this third example, ProcA creates a new dynamic component and puts it on a scenario path. This dynamic component is placed in SlotA but at the same time remains on the path (just like a person can potentially occupy multiple roles at the same time in an organisation). A distinct copy is then placed in SlotB. Finally, ProcB destroys the original dynamic component by removing it from the path. This also means that SlotA is no longer occupied. However, SlotB is still populated by a copy of the original instance and is unaffected by the destroy action.

This last example illustrates how dynamic responsibilities can also be used to express mobile and dynamic behaviour. A plug-in is first taken out a pool of plug-ins (get) and then plugged in a dynamic stub (plug). The plug-in is executed (if the selection policy of the stub allows it). It is then removed from the stub (remove) and put back in the pool (store).

# Annotations

Annotations represent a general mechanism by which structured information can be attached to models, components, and paths. The annotations element is part of a URN specification. In a ucm-model, performance (response time) requirements and functional goals can be described in terms of these annotations. These categories of annotations are described in Sections 12.1 and 12.2 respectively.

## Performance requirements

Performance requirements are composed of response-time requirements attached to scenario paths through timestamps. A timestamp-point is a hyperedge (Section 8) with a visual orientation attribute that describes, in degrees (0º for right, 90º for up, etc.), the orientation of the construct. A timestamp may also indicate whether it is used as a reference to the start of a performance requirement (next) or to its end (previous).

A response-time requirement (response-time-req) contains references to two timestamps (starting and ending timestamp points), a name, and a description. The attribute response-time indicates the required response time between the two timestamps (in s) for a certain percentage of the responses.

Creating performance models from such requirements often necessitates the presence of an execution environment, e.g. devices and storage methods. Such an environment can be described at the beginning of a URN specification in the nfr-definitions. This element contains directories of devices and of data stores. A device has a name, a unique identifier, a description and a type (e.g. processor, disk, DSP, or other). A device may also have a predefined operation time (op-time). The data-store-directory contains data stores and access modes. data-store items and access-mode items have a unique identifier, a name and a description.

To enable performance analysis at the requirements level, responsibilities on a path can be linked to devices and can use data stores and access modes (see Section 11). Responsibility definitions have a data-store-spec, which defines how a data store is accessed through pairs of <reference to data-store, reference to access-mode>, and a service-request-spec, which contains a list of service requests. The latter are composed of a reference to a device (service-type) coupled with a user-defined quantity (request-number).

### XML definition

<!ELEMENT annotations (response-time-requirements?, agent-annotations?)>

<!ELEMENT response-time-requirements (response-time-req)*>

<!ELEMENT response-time-req EMPTY>

<!ATTLIST response-time-req

timestamp1        IDREF   #REQUIRED

timestamp2        IDREF   #REQUIRED

resptime-name     CDATA   #IMPLIED

response-time     NMTOKEN #REQUIRED

percentage        NMTOKEN #REQUIRED

description       CDATA   #IMPLIED >

<!ELEMENT timestamp-point EMPTY>

<!ATTLIST timestamp-point

orientation       NMTOKEN            #IMPLIED

reference         (previous | next)  #IMPLIED >

<!ELEMENT nfr-definitions (grl-concept-base, device-directory?,

data-store-directory?)>

<!ELEMENT device-directory (device)*>

<!ELEMENT device EMPTY>

<!ATTLIST device

device-id         ID                         #REQUIRED

device-type       (processor|disk|dsp|other) #REQUIRED

device-name       CDATA                      #IMPLIED

description       CDATA                      #IMPLIED

op-time           NMTOKEN                    #IMPLIED >

<!ELEMENT data-store-directory (data-store*, access-mode*)?>

<!ELEMENT data-store EMPTY>

<!ATTLIST data-store

data-store-id     ID      #REQUIRED

data-store-item   CDATA   #IMPLIED

description       CDATA   #IMPLIED >

<!ELEMENT access-mode EMPTY>

<!ATTLIST access-mode

access-mode-id    ID      #REQUIRED

access-mode-item  CDATA   #IMPLIED

description       CDATA   #IMPLIED >

<!ELEMENT data-store-spec (data-store-access)*>

<!ELEMENT data-store-access EMPTY>

<!ATTLIST data-store-access

data-store-id     IDREF   #REQUIRED

access-mode-id    IDREF   #REQUIRED >

<!ELEMENT service-request-spec (service-request)*>

<!ELEMENT service-request EMPTY>

<!ATTLIST service-request

service-type      IDREF   #REQUIRED

request-number    CDATA   #REQUIRED >

### Graphical notation

A timestamp point is shown as an arrowhead pointed towards the path where it is located. The hyperedge-name attribute of this hyperedge is shown as a label.

Because they are mostly definitions and annotations, the other elements presented in this section do not have a graphical annotation.

## Functional goals

The second type of annotation considered in UCMs relates to functional requirements goals in agent systems. An fr-goal contains two references to goal tags (starting and ending goal tags), preconditions and post-conditions, a unique identifier, a name, and a description. A goal-tag is similar in nature to a timestamp point: it is a hyperedge with an orientation attribute. However, the purpose of goal tags is to indicate on a path where explicit functional requirements goals are defined.

### XML definition

<!ELEMENT agent-annotations (fr-goal-list)>

<!ELEMENT fr-goal-list (fr-goal)*>

<!ELEMENT fr-goal (precondition-list?, postcondition-list?)>

<!ATTLIST fr-goal

start-point  IDREF   #REQUIRED

end-point    IDREF   #REQUIRED

fr-goal-id   ID      #IMPLIED

fr-goal-name CDATA   #IMPLIED

description  CDATA   #IMPLIED >

<!ELEMENT goal-tag EMPTY>

<!ATTLIST goal-tag

orientation NMTOKEN #IMPLIED >

### Graphical notation

A goal tag is shown as small square with a thick border located on a path. The hyperedge-name attribute of this hyperedge is shown as a label.

Because they are mostly annotations, the other elements presented in this section do not have a graphical annotation

# Scenario Definitions

Scenario definitions make use of path variables and conditions to identify individual scenarios in an integrated collection of UCMs. Once defined, such scenarios can be grouped or used for highlighting specific paths or for generating other representations such as Message Sequence Charts or TTCN test cases.

Note: the simple path data model and the scenario groups and definitions are still under heavy development.

## Path variables

The path data model is defined using Boolean global variables that remain unchanged once initialized. A path-variable-list defines all available variables with a name and a unique identifier.

### XML definition

<!ELEMENT path-variable-list (boolean-variable)*>

<!ELEMENT boolean-variable EMPTY >

<!ATTLIST boolean-variable

name           NMTOKEN  #REQUIRED

boolvar-id     ID       #REQUIRED>

### Graphical notation

No graphical notation is required for these DTD elements.

## Scenarios and groups

An individual scenario (scenario-definition) can be defined by initializing a list of Boolean variables (variable-init) and by providing a name and a specific start point (start-id) on a specific map (map-id). Scenario definitions can be grouped for management purpose under scenario-group, and all groups are found under scenario-list.

### XML definition

<!ELEMENT scenario-list (scenario-group)* >

<!ELEMENT scenario-group (scenario-definition)* >

<!ATTLIST scenario-group

name         NMTOKEN   #REQUIRED

description  CDATA     #IMPLIED >

<!ELEMENT scenario-definition (variable-init)* >

<!ATTLIST scenario-definition

name         NMTOKEN   #REQUIRED

map-id       IDREF     #IMPLIED

start-id     IDREF     #IMPLIED

description  CDATA     #IMPLIED >

<!ELEMENT variable-init EMPTY >

<!ATTLIST variable-init

variable-id  IDREF     #REQUIRED

value        NMTOKEN   #REQUIRED >

### Graphical notation

No graphical notation is required for these DTD elements.

# Static semantic constraints and well-formedness rules

This section presents a set of static semantic constraints and well-formedness rules, related to identifier references and hyperedge connectivity that UCM specifications need to satisfy. Constraints on the structure of a URN specification already enforced by the URN DTD are not repeated in this section. Note that the following set of constraints is sound but not exhaustive: an unsatisfied constraint demonstrates that the UCM specification is not well formed, whereas some UCM specifications could be not well formed even when all these constraints are satisfied.

## References to identifiers

In any XML DTD, attributes of type IDREF must refer to an existing attribute of type ID. Table 1/Z.152 further refines this constraint by specifying the exact attribute referenced by attributes of type IDREF.

Constraints on referenced identifiers

| Element | IDREF Attribute | Referenced Element | Referenced ID Attribute | Additional Constraints |
| --- | --- | --- | --- | --- |
| component-ref | component-parent | component-ref | component-ref-id | Both elements in the same structure-spec |
|  | referenced-component | component | component-id |  |
| data-store-access | access-mode-id | access-mode | access-mode-id |  |
|  | data-store-id | data-store | data-store-id |  |
| enforce-bindings | stub-id | hyperedge | hyperedge-id | Both elements in the same hypergraph |
| fr-goal | start-point | hyperedge | hyperedge-id | hyperedge is a goal-tag |
|  | end-point | hyperedge | hyperedge-id | hyperedge is a goal-tag |
| hyperedge-connection | source-hyperedge | hyperedge | hyperedge-id | Both elements in the same hypergraph |
| hyperedge-ref | hyperedge-id | hyperedge | hyperedge-id | Both elements in the same hypergraph |
| in-connection | hyperedge-id | hyperedge | hyperedge-id | hyperedge is a start from another ucm-model in plug-in-maps |
|  | stub-entry-id | stub-entry | stub-entry-id |  |
| out-connection | hyperedge-id | hyperedge | hyperedge-id | hyperedge is an end-point from another ucm-model in plug-in-maps |
|  | stub-exit-id | stub-exit | stub-exit-id |  |
| path-binding | stub-entry-id | stub-entry | stub-entry-id | stub-entry and stub-exit belong to same stub |
|  | stub-exit-id | stub-exit | stub-exit-id |  |
| path-branching-characteristic | empty-segment | hyperedge | hyperedge-id | hyperedge is an empty-segment |
| path-branching-spec | fork-id | hyperedge | hyperedge-id | hyperedge is a fork |
| plug-in-binding | parent-map-id | ucm-model | ucm-model-id |  |
|  | stub-id | hyperedge | hyperedge-id | hyperedge is a stub |
|  | submap-id | ucm-model | ucm-model-id | ucm-model is in plug-in-maps |
| plug-in-pool | ucm-model-id | ucm-model | ucm-model-id | ucm-model is in plug-in-maps |
|  | pool-id | component | component-id | component is a pool |
| regular | processor-id | device | device-id | device-type is processor |
| response-time-req | timestamp1 | hyperedge | hyperedge-id | hyperedge is a timestamp-point |
|  | timestamp2 | hyperedge | hyperedge-id | hyperedge is a timestamp-point |
| responsibility-ref | resp-id | responsibility | resp-id |  |
| scenario-definitions | map-id | ucm-model | ucm-model-id |  |
|  | start-id | hyperedge | hyperedge-id | hyperedge is a start on ucm-model map-id |
| service-request | service-type | device | device-id |  |
| stub-entry | hyperedge-id | hyperedge | hyperedge-id | hyperedge is an empty-segment |
| stub-exit | hyperedge-id | hyperedge | hyperedge-id | hyperedge is an empty-segment |
| variable-init | variable-id | boolean-variable | boolvar-id |  |

## Well-formed rules for hypergraphs

Table 2/Z.152  defines the constraints on how hyperedges can be connected together in order to form a well-formed hypergraph. For each type of hyperedge, the number of source/target hyperedges for normal path connections and for interpath connections are specified, together with the types allowed. In general, empty-segment hyperedges are required between any two hyperedges of the other types, except for the connect and abort hyperedges. A cardinality of the form x-N means that the minimum is x and there is no maximum.

Constraints on hyperedge connectivity

| Hyperedge type | Normal path connections | Interpath connections |
| --- | --- | --- |
|  | # Sources | # Targets | # Sources | # Targets |
| start | 0 | 1 (empty-segment) | 0-N (connect) | 0 |
| end-point | 1 (empty-segment) | 0 | 0 | 0-N (connect) |
| responsibility-ref | 1 (empty-segment) | 1 (empty-segment) | 0 | 0 |
| fork | 1 (empty-segment) | 2-N (empty-segment) | 0 | 0 |
| join | 2-N (empty-segment) | 1 (empty-segment) | 0 | 0 |
| synchronization | 1-N (empty-segment) | 1-N (empty-segment) | 0 | 0 |
| loop | 2 (empty-segment) | 2 (empty-segment) | 0 | 0 |
| stub | 1-N (empty-segment) | 1-N (empty-segment) | 0-N (abort) | 0-N (abort) |
| waiting-place | 1 (empty-segment) | 1 (empty-segment), plus 0-1 (abort) for timeout path | 0-N (connect) | 0 |
| abort | 0 | 0 | 1 (stub or emtpy-segment) | 1 (stub or emtpy-segment) |
|  | 1 (waiting-place/timer) | 1 (empty-segment) | 0 | 0 |
| connect | 0 | 0 | 1 (end-point or empty-segment) | 1 (start or waiting-place) |
| timestamp-point | 1 (empty-segment) | 1 (empty-segment) | 0 | 0 |
| goal-tag | 1 (empty-segment) | 1 (empty-segment) | 0 | 0 |
| empty-segment | 1 (any hyperedge except end-point and connect) | 1 (any hyperedge except start, abort and connect) | 0-N (abort) | 0-N (connect or abort) |

# Dynamic semantics

TO BE PROVIDED

Full-fledged formal languages often have a well-defined dynamic semantics. Whether a single dynamic semantics is desirable in a requirements language remains a question for further study. If one is defined, it should be done in a way that would enable simple transformations towards other languages such as UML, MSC, SDL, and TTCN.

# Compliance statement

The following table describes the requirements for URN-FR as described in Z.150, together with an assessment of how well the UCM notation conforms to these requirements.

UCM compliance table

| ID | Requirement | Type | R/O | Depends On | Conf Status | Explanation |
| --- | --- | --- | --- | --- | --- | --- |
| 00100 | Specify the set of input events at scenario start point | FR | R |  | C |  |
| 00200 | Specify the set of output events at scenario end point | FR | R |  | C |  |
| 00300 | Specify preconditions at scenario start points | FR | R |  | C |  |
| 00400 | Specify post-conditions at scenario end points | FR | R |  | C |  |
| 00500 | Identify input sources, that is, whether the sources are human or machine | FR | R |  | N |  |
| 00600 | Identify output sources, that is, whether the sources are human or machine | FR | R |  | N |  |
| 00700 | Specify system operations in terms of a causal flow of responsibilities | FR | R |  | C |  |
| 00800 | Specify alternative courses of action within a scenario | FR | R |  | C |  |
| 00900 | Specify repetitive action within a scenario | FR | R |  | C |  |
| 01000 | Specify parallel courses of action within a scenario | FR | R |  | C |  |
| 01100 | Specify synchronization within a scenario | FR | R |  | C |  |
| 01200 | Specify synchronization between scenarios | FR | R |  | C |  |
| 01300 | Specify a lengthy scenario by way of a root map and references to child maps; child maps may have children | FR | R |  | C |  |
| 01301 | Specify preconditions at the entry points to a child map | FR | R |  | C |  |
| 01302 | Specify post-conditions at the exit points from a child map | FR | R |  | C |  |
| 01400 | Group related scenarios | FR | R |  | C |  |
| 01450 | Specify individual scenarios | FR | R |  | C |  |
| 01500 | Specify feature interactions | FR | R |  | C |  |
| 01600 | Specify scenarios without reference to components | FR | R |  | C |  |
| 01700 | Specify scenarios with reference to components and the allocation of responsibilities to components | FR | R |  | C |  |
| 01800 | Specify scenarios with reference to Commercial-Off-The-Shelf (COTS) components | FR | R |  | C |  |
| 01900 | Specify scenarios with reference to conceptual components | FR | R |  | C |  |
| 02000 | Specify the behaviour of the system’s environment | FR | R |  | C | Same requirements as for specifying scenarios |
| 02100 | Elicit requirements, that is, use the notation to reason about domain knowledge | FR | R |  | C |  |
| 02200 | Cross-reference operationalizations in the NFR model to responsibilities in the FR model | B | R |  | C | Through attributes and non-intentional elements which are responsibilities. |
| 02300 | Cross-reference performance constraints identified in the NFR model to responsibilities or scenarios in the FR model | B | R |  | C | Through attributes of performance softgoal and non-intentional elements which are responsibilities and scenarios. |

UCM Document Type Definition

<!--  This part from Z.150 / URN  -->

<!ELEMENT urn-spec (definitions?, urn-nfr-spec?, urn-fr-spec?,

annotations?)>

<!ATTLIST urn-spec

spec-id             ID      #REQUIRED

dtd-version         NMTOKEN #REQUIRED

spec-name           CDATA   #IMPLIED

component-notation  NMTOKEN "Buhr-UCM"

data-language       NMTOKEN "none"

width               NMTOKEN "1320"

height              NMTOKEN "1100"

description         CDATA   #IMPLIED >

<!ELEMENT definitions (component-definitions?, responsibility-definitions?,

nfr-definitions?)>

<!--  This part from Z.151 / GRL  -->

<!ELEMENT nfr-definitions (element-definitions, device-directory?,

data-store-directory?)>

<!--  This part is new, from Z.152 / UCM  -->

<!ELEMENT urn-fr-spec (root-maps, plug-in-maps?, plug-in-bindings?,

path-variable-list?, scenario-list?)>

<!ELEMENT root-maps (ucm-model)+>

<!ELEMENT plug-in-maps (ucm-model)*>

<!ELEMENT ucm-model (path-spec?, structure-spec?)>

<!ATTLIST ucm-model

ucm-model-id   ID      #REQUIRED

ucm-model-name CDATA   #REQUIRED

title          CDATA   "No title"

description    CDATA   #IMPLIED >

<!ELEMENT path-spec (hypergraph)?>

<!ELEMENT hypergraph (hyperedge*, hyperedge-connection*,

path-branching-spec*, enforce-bindings*)>

<!ELEMENT hyperedge ( (start | end-point | responsibility-ref |

fork | join | synchronization | loop | stub |

waiting-place | abort | connect | timestamp-point |

goal-tag | empty-segment)) >

<!ATTLIST hyperedge

hyperedge-id     ID      #REQUIRED

hyperedge-name   CDATA   #IMPLIED

fx               NMTOKEN #IMPLIED

fy               NMTOKEN #IMPLIED

lx               NMTOKEN #IMPLIED

ly               NMTOKEN #IMPLIED

description      CDATA   #IMPLIED >

<!ELEMENT hyperedge-connection (hyperedge-ref)*>

<!ATTLIST hyperedge-connection

source-hyperedge IDREF   #REQUIRED >

<!ELEMENT hyperedge-ref EMPTY>

<!ATTLIST hyperedge-ref

hyperedge-id     IDREF   #REQUIRED >

<!ELEMENT start (triggering-event-list?, precondition-list?)?>

<!ATTLIST start

arrival     (exponential | deterministic

| uniform | erlang

| expert | none)          "none"

mean                NMTOKEN            #IMPLIED

value               NMTOKEN            #IMPLIED

low                 NMTOKEN            #IMPLIED

high                NMTOKEN            #IMPLIED

kernel              NMTOKEN            #IMPLIED

expert-distribution CDATA              #IMPLIED >

<!ELEMENT triggering-event-list (event)*>

<!ATTLIST triggering-event-list

composition         CDATA              "OR" >

<!ELEMENT end-point (resulting-event-list?, postcondition-list?)?>

<!ELEMENT resulting-event-list (event)*  >

<!ATTLIST resulting-event-list

composition         CDATA              "AND" >

<!ELEMENT postcondition-list (condition)*>

<!ATTLIST postcondition-list

composition CDATA   "AND" >

<!ELEMENT precondition-list (condition)*>

<!ATTLIST precondition-list

composition CDATA   "AND" >

<!ELEMENT condition EMPTY>

<!ATTLIST condition

name        NMTOKEN  #REQUIRED

description CDATA    #IMPLIED >

<!ELEMENT event EMPTY>

<!ATTLIST event

name        NMTOKEN  #REQUIRED

description CDATA    #IMPLIED >

<!ELEMENT responsibility-ref EMPTY>

<!ATTLIST responsibility-ref

resp-id        IDREF     #REQUIRED

arrow-position NMTOKEN   #IMPLIED >

<!ELEMENT fork EMPTY>

<!ATTLIST fork

orientation NMTOKEN #IMPLIED >

<!ELEMENT join EMPTY>

<!ATTLIST join

orientation NMTOKEN #IMPLIED >

<!ELEMENT synchronization EMPTY>

<!ATTLIST synchronization

cardinality-source  NMTOKEN #IMPLIED

cardinality-target  NMTOKEN #IMPLIED

orientation         NMTOKEN #IMPLIED >

<!ELEMENT loop EMPTY>

<!ATTLIST loop

orientation    NMTOKEN #REQUIRED

exit-condition CDATA   #IMPLIED >

<!ELEMENT stub (stub-entry-list, stub-exit-list, precondition-list?,

postcondition-list?, service-request-spec?)>

<!ATTLIST stub

type              (static | dynamic)  "static"

shared            (yes | no)          "no"

selection-policy  CDATA               #IMPLIED>

<!ELEMENT stub-entry-list (stub-entry)+>

<!ELEMENT stub-entry EMPTY>

<!ATTLIST stub-entry

stub-entry-id   ID      #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

<!ELEMENT stub-exit-list (stub-exit)+>

<!ELEMENT stub-exit EMPTY>

<!ATTLIST stub-exit

stub-exit-id    ID      #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

<!ELEMENT waiting-place (triggering-event-list?, precondition-list?)?>

<!ATTLIST waiting-place

timer           (yes | no)    "no"

wait-type       CDATA       #IMPLIED >

<!ELEMENT abort EMPTY>

<!ELEMENT connect EMPTY>

<!ELEMENT empty-segment (precondition-list?, postcondition-list?)?>

<!ATTLIST empty-segment

path-label      CDATA                      #REQUIRED

characteristics (failure-point | shared

| direction-arrow )       #IMPLIED

show-label      (yes | no)                 "no" >

<!ELEMENT path-branching-spec (path-branching-characteristic)*>

<!ATTLIST path-branching-spec

fork-id    IDREF   #REQUIRED >

<!ELEMENT path-branching-characteristic EMPTY>

<!ATTLIST path-branching-characteristic

characteristic  CDATA   #IMPLIED

branch-condition CDATA   #IMPLIED

probability     NMTOKEN #IMPLIED

empty-segment   IDREF   #REQUIRED

lx              NMTOKEN #IMPLIED

ly              NMTOKEN #IMPLIED >

<!ELEMENT component-definitions (component)*>

<!ELEMENT component ((regular | pool))>

<!ATTLIST component

component-id        ID          #REQUIRED

component-name      CDATA       #REQUIRED

description         CDATA       #IMPLIED

colour              NMTOKEN     #IMPLIED >

<!ELEMENT regular EMPTY>

<!ATTLIST regular

type                NMTOKEN     "team"

protected           (yes | no)  "no"

slot                (yes | no)  "no"

replicated          (yes | no)  "no"

replication-factor  NMTOKEN     "1"

processor-id        IDREF       #IMPLIED >

<!ELEMENT pool EMPTY>

<!ATTLIST pool

type                NMTOKEN  #REQUIRED >

<!ELEMENT structure-spec (component-ref)* >

<!ELEMENT component-ref (responsibility-list?, other-hyperedge-list?)?>

<!ATTLIST component-ref

component-ref-id      ID          #REQUIRED

referenced-component  IDREF       #IMPLIED

component-parent      IDREF       #IMPLIED

role                  CDATA       #IMPLIED

fx                    NMTOKEN     #REQUIRED

fy                    NMTOKEN     #REQUIRED

width                 NMTOKEN     #REQUIRED

height                NMTOKEN     #REQUIRED

anchored              (yes | no)  "no"  >

<!ELEMENT responsibility-list (hyperedge-ref)*>

<!ELEMENT other-hyperedge-list (hyperedge-ref)*>

<!ELEMENT plug-in-bindings (plug-in-binding*, plug-in-pool*)? >

<!ELEMENT plug-in-binding (in-connection-list?, out-connection-list?)?>

<!ATTLIST plug-in-binding

parent-map-id    IDREF   #REQUIRED

submap-id        IDREF   #REQUIRED

stub-id          IDREF   #REQUIRED

branch-condition CDATA   #IMPLIED>

<!ELEMENT in-connection-list (in-connection)*>

<!ELEMENT in-connection EMPTY>

<!ATTLIST in-connection

stub-entry-id   IDREF   #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

<!ELEMENT out-connection-list (out-connection)*>

<!ELEMENT out-connection EMPTY>

<!ATTLIST out-connection

stub-exit-id    IDREF   #REQUIRED

hyperedge-id    IDREF   #REQUIRED >

<!ELEMENT plug-in-pool EMPTY>

<!ATTLIST plug-in-pool

pool-id         IDREF   #REQUIRED

ucm-model-id    IDREF   #REQUIRED >

<!ELEMENT enforce-bindings (path-binding)*>

<!ATTLIST enforce-bindings

stub-id         IDREF   #REQUIRED >

<!ELEMENT path-binding EMPTY>

<!ATTLIST path-binding

stub-entry-id   IDREF   #REQUIRED

stub-exit-id    IDREF   #REQUIRED >

<!ELEMENT responsibility-definitions (responsibility)*>

<!ELEMENT responsibility (data-store-spec?, service-request-spec?,

(precondition-list?, postcondition-list?)?,

dynamic-resp?)?>

<!ATTLIST responsibility

resp-id         ID      #REQUIRED

resp-name       CDATA   #IMPLIED

exec-sequence   CDATA   #IMPLIED

description     CDATA   #IMPLIED >

<!ELEMENT dynamic-resp EMPTY>

<!ATTLIST dynamic-resp

type         (move | move-stay | create

| copy | destroy)         #REQUIRED

direction    (in | out)                  #REQUIRED

sourcepool   CDATA                       #IMPLIED

arrow-length NMTOKEN                     #IMPLIED >

<!ELEMENT annotations (response-time-requirements?, agent-annotations?)>

<!ELEMENT response-time-requirements (response-time-req)*>

<!ELEMENT response-time-req EMPTY>

<!ATTLIST response-time-req

timestamp1        IDREF   #REQUIRED

timestamp2        IDREF   #REQUIRED

resptime-name     CDATA   #IMPLIED

response-time     NMTOKEN #REQUIRED

percentage        NMTOKEN #REQUIRED

description       CDATA   #IMPLIED >

<!ELEMENT timestamp-point EMPTY>

<!ATTLIST timestamp-point

orientation       NMTOKEN            #IMPLIED

reference         (previous | next)  #IMPLIED >

<!ELEMENT device-directory (device)*>

<!ELEMENT device EMPTY>

<!ATTLIST device

device-id         ID                         #REQUIRED

device-type       (processor|disk|dsp|other) #REQUIRED

device-name       CDATA                      #IMPLIED

description       CDATA                      #IMPLIED

op-time           NMTOKEN                    #IMPLIED >

<!ELEMENT data-store-directory (data-store*, access-mode*)?>

<!ELEMENT data-store EMPTY>

<!ATTLIST data-store

data-store-id     ID      #REQUIRED

data-store-item   CDATA   #IMPLIED

description       CDATA   #IMPLIED >

<!ELEMENT access-mode EMPTY>

<!ATTLIST access-mode

access-mode-id    ID      #REQUIRED

access-mode-item  CDATA   #IMPLIED

description       CDATA   #IMPLIED >

<!ELEMENT data-store-spec (data-store-access)*>

<!ELEMENT data-store-access EMPTY>

<!ATTLIST data-store-access

data-store-id     IDREF   #REQUIRED

access-mode-id    IDREF   #REQUIRED >

<!ELEMENT service-request-spec (service-request)*>

<!ELEMENT service-request EMPTY>

<!ATTLIST service-request

service-type      IDREF   #REQUIRED

request-number    CDATA   #REQUIRED >

<!ELEMENT agent-annotations (fr-goal-list)>

<!ELEMENT fr-goal-list (fr-goal)*>

<!ELEMENT fr-goal (precondition-list?, postcondition-list?)>

<!ATTLIST fr-goal

start-point  IDREF   #REQUIRED

end-point    IDREF   #REQUIRED

fr-goal-id   ID      #IMPLIED

fr-goal-name CDATA   #IMPLIED

description  CDATA   #IMPLIED >

<!ELEMENT goal-tag EMPTY>

<!ATTLIST goal-tag

orientation NMTOKEN #IMPLIED >

<!ELEMENT path-variable-list (boolean-variable)*>

<!ELEMENT boolean-variable EMPTY >

<!ATTLIST boolean-variable

name          NMTOKEN  #REQUIRED

boolvar-id    ID       #REQUIRED >

<!ELEMENT scenario-list (scenario-group)* >

<!ELEMENT scenario-group (scenario-definition)* >

<!ATTLIST scenario-group

name         NMTOKEN   #REQUIRED

description  CDATA     #IMPLIED >

<!ELEMENT scenario-definition (variable-init)* >

<!ATTLIST scenario-definition

name         NMTOKEN   #REQUIRED

map-id       IDREF     #IMPLIED

start-id     IDREF     #IMPLIED

description  CDATA     #IMPLIED >

<!ELEMENT variable-init EMPTY >

<!ATTLIST variable-init

variable-id  IDREF     #REQUIRED

value        NMTOKEN   #REQUIRED

Use Case Maps Tutorial

This informative annex contains tutorials and illustrative examples that supplement the specification of the Use Case Map notation. This notation is used for describing causal relationships between responsibilities, which may potentially be bound to underlying organizational structures of abstract components. The resulting visual scenarios are called Use Case Maps (UCMs) or simply maps. Responsibilities are generic and can represent actions, activities, operations, tasks to perform, and so on. Components are also generic and can represent software entities (objects, processes, databases, servers, functional entities, network entities, etc.) as well as non-software entities (e.g. users, actors, processors). The relationships are said to be causal because they involve concurrency and partial orderings of activities and because they link causes (e.g., preconditions and triggering events) to effects (for example post-conditions and resulting events). In a way, UCMs show related use cases in a map-like diagram.

UCMs uses behaviour as a concrete, first-class architectural concept. Maps usually emphasize the most relevant, interesting, and critical functionalities of the system, even when little design information is available. With the UCM notation, scenarios are expressed above the level of messages exchanged between components; hence they are not necessarily bound to a specific underlying structure. UCMs provides a path-centric view of system functionalities and improves the level of reusability of scenarios. The notation also enables scenario integration at various levels, architectural reasoning, and description of dynamic behaviour and architectures.

In Stage 1 documents as defined in I.130 and Q.65, requirements usually suffer from heavy instabilities, whereas scenarios and potential component topologies are volatile. UCMs fit well in approaches that intend to bridge the gap between requirements and an abstract system design (Stage 2 document as defined in I.130 and Q.65), where a tentative distribution of system behaviour over a structure is being introduced. The generation of Stage 2 documents, which usually contain information flows or Message Sequence Charts, from UCM descriptions will hence briefly be addressed. Stage 3 documents as defined in I.130 and Q.65 describe the various protocols and procedures involved in the support of the MSCs described in the previous stage.

This tutorial illustrates some useful applications of the UCM notation to the following steps of systems and standards development processes:

Description of causal scenarios and architectures (Section B.1)

Architectural reasoning (Sections B.1 and B.2)

Refinements with Message Sequence Charts (Section B.2)

Scenario integration (Section B.3)

Description of highly dynamic systems (Section B.4)

Several telecommunication services and features will serve as illustrative examples.

Description of causal scenarios and architectures

Description of a simplified call screening scenario

The UCM notation is used to describe causal scenarios when little design information is available. The following example is based on a simplified version of a call-screening feature in a Wireless Intelligent Network system. Figure 4/Z.152 shows a map where an incoming call is tentatively initiated (IncomingCall, or IC). This causes a screening function to be executed according to the subscriber’s policies. In this map, two alternative results are considered. If the call initiator is on the receiver’s screening list (condition OnList), then an announcement is played (PlayBlockAnnounce, or PBA) and the call is blocked (CalledBlocked, or CB). Otherwise (condition NotOnList), there is no special treatment (NormalAlerting, or NA) and the call is accepted  (CallSetup, or CS). In order for the figures and labels to be more concise, the rest of the section will use abbreviations as labels and will not display the conditions on the OR-fork.

UCM description of a simplified call screening scenario

A UCM starts with a triggering event or a pre-condition (filled circle labeled IC) and ends with one or more resulting events or post-conditions (bars), in this case CS or CB. A route is a scenario that evolves on a path linking an initial cause to a final effect. Intermediate responsibilities (S, NA, and PBA) are activated along the way to form routes such as <IC, S, NA, CS>. Think of responsibilities as tasks to be performed. The notation allows for alternative paths (the OR-Fork in the figure), concurrent paths, exception paths, timers, stubs with plug-ins, and synchronous or asynchronous interactions between paths.

Such maps have proved to be very useful in Stage 1 descriptions of service functionalities. Their principal emphasis is on causality and responsibilities, without any reference to messages, system components, or component states. Yet, they represent useful and powerful tools for the support of the thinking process and the evaluation of functional alternatives. This causal dependence between responsibilities should be documented as early as possible in the design process, before this information gets lost among the details of the behaviour of individual components. This is especially true of concurrent, communicating, and distributed systems.

Evaluation of architectural alternatives for functional entities

UCM paths can be bound to various structures of components, which leads to a visual integration of scenarios and architecture in a single view. The UCM notation supports the reuse of scenarios when the underlying structure is modified or refined, even across architectural domains. For instance, Figure 5/Z.152(a) and Figure 5/Z.152(b) illustrate two sample structures of functional entities (FEs), which are the components of IN’s distributed functional plane. In this example, FEs are shown as processes, i.e. with parallelograms. The example scenario (Figure 4/Z.152) is bound differently to each collection of FEs. The same scenario can also be bound to the same structure, but in a different way, as shown in Figure 5/Z.152(c).

A causal scenario path bound to different structures of FEs

In Stage 2 descriptions, different potential structures could undergo some evaluation, hence enabling architectural reasoning. Scenarios described in terms of wired components, such as Message Sequence Charts or as sequence diagrams in the Unified Modelling Language (UML), would need to be rebuilt as soon as there is a change in the underlying structure, because the functionalities are tightly bound to how the structure looks like. UCMs scenarios are more reusable and require simpler modifications, consisting only of a new binding between the responsibilities and the components.

Refinements with Message Sequence Charts

When extracting MSC-like scenarios directly from informal requirements, as it is often done in conventional system development, many design decisions become buried in the details of the scenarios. For instance, Wireless Intelligent Network MSCs are often described in terms of network entities, which contain various functional entities. Design decisions such as the allocation of UCM responsibilities to functional entities (the logical components in the distributed functional model) and the allocation of functional entities to network entities (the physical entities in the network reference model) are lost. Assuming that such a standard does not impose a specific mapping of functional entities to network entities, different vendors who build network entities may use different mappings. Designers must reverse-engineer information and scenarios that would be explicit in a UCM view where responsibilities and other constructs are bound to functional entities. This delays the design and implementation phases and leads to multiple interoperability problems. Such problems are unfortunately common in standards.

By using a UCM view, many issues related to messages, protocols, communication constraints, and structural evolutions (e.g. from one version of the structure to the next) can be abstracted, and the focus can be put on intended functionalities and on reusable causal scenarios in their structural context. This section aims to illustrate the kind of design decisions that one needs to take and document when generating MSCs from UCM descriptions.

MSC refinements of bound maps

Bound UCMs can serve as a basis for the generation of correct MSCs in Stage 2 documents, provided that additional information related to communication constraints, protocols, and parameters are defined to refine inter-responsibliity causal relationships into inter-component message exchanges. Many MSCs could be valid according to a UCM, as long as the intended causal relationships between the responsibilities are satisfied. The following example uses Figure 5/Z.152(c), duplicated in Figure 6/Z.152(a), as a starting point.

Figure 6/Z.152(b) is a potential MSC extracted from the route <IC, S, NA, CS>, where the exchange of messages is minimal. Responsibilities are performed by the entities to which they are bound, so S and NA are actions performed by FE2. In this example, input and output events, captured by the start point IC and the end point CS, are interpreted as messages from and to the environment. The causal path linking FE1 to FE2 is refined by an appropriate exchange of messages between these two entities (e.g. the simple message m1). Different protocols could be used at this point, and the flow of data would need to be specified as well.

Figure 6/Z.152(c) is a potential MSC extracted from the route <IC, S, PBA, CB>. As implied by the multiple messages between FE2 to FE4, complex protocols or negotiation mechanisms could be involved between two given entities.

Generation of potential MSCs from scenario paths bound to a structure of FEs

Structural alternatives for functional entities and network entities

Moving from Stage 2 documents to Stage 3 documents requires  the functional entities to be bound to network entities (NEs), the components of IN’s physical plane. Again, different allocations are possible, and design decisions have to be made and documented. Two collections of NEs lead to different mappings in Figure 7/Z.152(a) and Figure 7/Z.152(b). In Figure 7/Z.152(c), the structure remains the same as in Figure 7/Z.152(b), but FE2 and FE3 are allocated differently.

Different bindings of functional entities to network entities

MSC refinements of bound maps with constrained communication mechanisms

The bound map in Figure 8/Z.152(a) results from the allocation of responsibilities to FEs described in Figure 5/Z.152(c) and from the allocation of FEs to NEs described in Figure 7/Z.152(c). Components may have restricted access to each other. This type of constraint is often defined by communication channels or interfaces linking the components. In this example, NE2 is allowed to communicate with both NE1 and NE3, but NE1 and NE3 cannot communicate directly. This is shown by the links between the various components (not part of the URN notation). Such constraints are often described in Stage 3 documents, hence paving the way towards protocols and procedures for the final architecture.

At this level, a new collection of MSCs can be generated, this time in terms of network entities. Figure 8/Z.152(b) is a potential MSC extracted from the route <IC, S, NA, CS>, where the exchange of messages is minimal. Notice how NE2 is used to refine the causal relationship between IC and S: NE1 is not allowed to send messages directly to NE3, but messages can be forwarded through NE2. Similarly, Figure 8/Z.152(c) is a potential MSC extracted from the route <IC, S, PBA, CB>, this time with a complex negotiation mechanism between NE2 and NE3, which may result from the negotiation between FEs as suggested by Figure 6/Z.152(c). Again, those MSCs are just potential candidates. Many other MSCs could refine the same map according to different choices in the communication constraints and protocols.

Generation of MSCs from scenario paths bound to a constrained structure of NEs

The types of decision discussed in this section are only relevant in a late stage of the development process. Yet, many standards and system descriptions include MSCs based on network entities (or the equivalent) in Stage 2, and sometimes even in preliminary Stage 1 documents, hence skipping many decision steps. This hurts the development process by not separating concerns, by narrowing the number of potential implementations too soon, and by not documenting any of the requirements and design decisions needed to enable adaptation and evolution.

Integration of scenarios

Scenarios are often described in isolation. However, at some point in time, a view where all scenarios are integrated together becomes important for analysis, for consistency checking, for the detection of interactions, and for the construction of more detailed models. This section contains a second example (unrelated to the call screening feature discussed so far) where three features, described as individual maps based on a simplified call initiation, are integrated into one map with sub-maps (plug-ins).

Simplified call initiation scenario

The following call initiation scenario is bound to a structure with two types of components, User and Agent, which can both assume one of two roles: originating (O) or terminating (T). The originating user initiates a call through the start point req (Figure 9/Z.152). The terminating agent verifies whether the terminating user is busy or idle (vrfy). When idle, the terminating user status is updated in its agent (upd) and a resulting ringing event occurs at the terminating user side (ring). Simultaneously, this results in an event at the originating user side (sig) signaling a prepared ringback reply (prb). When busy, a busy reply is prepared (pb) and a corresponding signaling event results at the originating user side.

Simplified call initiation UCM

This UCM already integrates multiple sequential scenarios through path elements like OR-forks and AND-forks.

Three features described in isolation

Often, telecommunications features are described in terms of an underlying basic call. The following three features extend the simplified basic call UCM to include new functionalities or prevent existing ones.

The first feature is the originating call screening (OCS), described in Figure 10/Z.152. The originating agent possesses a screening list object (OCSlist) that is checked (chk) to determine whether the call should be allowed or denied. When allowed, the call initiation scenario continues. When denied, a denied reply is prepared (pd) and a corresponding signaling event results at the originating user side.

Originating call screening (OCS) feature UCM

The UCM in Figure 11/Z.152 describes the TeenLine feature, located in the originating agent. This feature checks the current time (chkTime) to determine whether the call is being initiated at a specific time of the day. When in the predefined range, TeenLine requires a valid personal identification number (PIN) to be provided in a timely fashion for the call initiation to continue. If an invalid PIN is provided, or if a time-out occurs, then a denied reply is prepared (pd).

TeenLine feature UCM

Figure 12/Z.152 presents the third feature, Call number delivery (CND), located at the terminating side. This feature displays (disp) the name of the calling party, i.e. the originating user.

Call number delivery (CND) feature UCM

Integrated scenarios

UCMs can help structuring and integrating scenarios in various ways, e.g. sequentially, as alternatives (with OR-forks/joins) or concurrently (with AND-forks/joins). However, one of the most interesting constructs for scenario integration is certainly the stub. While static stubs contain only one sub-map (plug-in), dynamic stubs may contain multiple sub-maps whose selection can be determined at run-time according to a selection policy. Such a policy can make use of preconditions, assertions, run-time information, composition operators, etc. in order to select the plug-in(s) to use. Selection policies are described with a (formal or informal) language suitable for the context where they are used. The plug-in maps are sub-maps that describe locally how a feature modifies the basic behaviour. Multiple levels of stubs and plug-ins can be used.

A potential root map that integrates the three features seen so far is presented in Figure 13/Z.152. Stub SO contains the originating features whereas stub ST contains a single plug-in (illustrating scenario decomposition), which in turn will possess a stub (SD) for the terminating features. Each of these stubs includes plug-ins that represent how the call initiation reacts in the presence or absence of features.

Root map for integrated call initiation

Five plug-ins are presented in Figure 14/Z.152. These sub-maps are connected directly or indirectly to the Root map of Figure 13/Z.152 in order to support the features and the basic call initiation. By default, these plug-ins act locally in the component where the parent stub is located. If a component outside the containing component is referenced by the plug-in (e.g. User:T in Figure 14/Z.152(e)), then this component needs to be declared as anchored. Such components have a shadow at the bottom to indicate visually that they are already defined elsewhere.

Plug-ins for the various features

The binding relationships, which are used to connect plug-ins to stubs, are enumerated in Table 4/Z.152 . Through these relationships, it is possible to reconstruct the initial UCMs:

Simplified call initiation (Figure 9/Z.152): Default in SO, Terminating in ST, Default in SD.

OCS feature (Figure 10/Z.152): OCS in SO, Terminating in ST, Default in SD.

TeenLine feature (Figure 11/Z.152): TeenLine in SO, Terminating in ST, Default in SD.

CND feature (Figure 12/Z.152): Default in SO, Terminating in ST, CND in SD.

Binding relationships for integrated view

| Parent map | Stub | Plug-in map | Figure 14/Z.152 | Binding relationship |
| --- | --- | --- | --- | --- |
| Root | SO | Default | (a) | {<IN1, Din1>, <OUT1, Dout1>} |
|  |  | TeenLine | (b) | {<IN1, Tin1>, <OUT1, Tout1>, <OUT2, Tout2>} |
|  |  | OCS | (c) | {<IN1, Oin1>, <OUT1, Oout1>, <OUT2, Oout2>} |
|  | ST | Terminating | (d) | {<IN2, in2>, <OUT3, out3>, <OUT4, out4>} |
| Terminating | SD | Default | (a) | {<IN3, Din1>, <OUT5, Dout1>} |
|  |  | CND | (e) | {<IN3, Cin1>, <OUT5, Cout1>} |

Adding features to such UCM collections is often achieved by creating new plug-ins for the existing stubs, or by adding new stubs containing either new plug-ins or instances of existing plug-ins. In all cases, the selection policies need to be updated appropriately.

Feature interactions and selection policies

Dynamic stubs contain selection policies used to determine which plug-in(s) should be selected at run-time. For stub SD, a potential policy could be as simple as this condition:

IF subscribed(User:T, CND)

THEN select CND

ELSE select  Default

ENDIF

However, things are slightly more complex for stub SD, which contains three plug-ins. Both OCS and TeenLine can easily have priority over Default, but there exists an interaction between these two features that requires a resolution. Stubs and selection policies tend to localize the places on scenarios where undesirable feature interactions can occur, hence simplifying the analysis and the resolution of these undesirable interactions. Among other things, they can be used to specify priorities of some features over others. For instance, TeenLine could be given precedence over OCS in stub SO. One feature could even prevent another feature from being executed. Many spurious interactions between features are thus avoided by structuring and integrating the scenarios in the proper context.

In our particular example, one potential policy could be:

IF subscribed(User:O, OCS)

THEN 	IF subscribed(User:O, TeenLine)

THEN select TeenLine ; select OCS

ELSE select OCS

ENDIF

ELSE 	IF subscribed(User:O, TeenLine)

THEN select TeenLine

ELSE select Default

ENDIF

ELSE select  Default

ENDIF

Although it works in this case, this type of policy does not scale well when there is a large number of plug-ins. Mechanisms based on assertions and concurrent negotiation between plug-ins have the potential of coping with this issue.

Description of highly dynamic systems

Highly dynamic systems are usually difficult to represent using a static notation. Section B.3 already presented how dynamically "pluggable" behaviour can be described using dynamic stubs. However, describing self-modifying architecture and mobile behaviour remains a major challenge. The following two examples present how UCMs can be used to address this issue.

Description of dynamic architectures

This example makes use of slots, pools, and dynamic responsibilities to demonstrate the expressiveness of these concepts in a dynamic architecture context. A hypothetical telephony system is composed of a telephone switch, containing multiple devices, and of a provisioning site responsible for the creation, storage, and retrieval of device handlers (Figure 15/Z.152). The switch contains devices, which perform telephony operations, and a driver process, which requests and installs required device handlers. The provisioning site contains a server process that decodes requests for new handlers, and a supplier process where new device handlers are created. These handlers are stored for future use in a repository, represented in the map by a pool of objects.

Dynamic device handler map

The scenario path on the left can be interpreted intuitively as follows. Upon the shipment of a new device, Supplier creates a new handler object and then stores it in the Handlers pool. At this point, this new handler is available to the switch. The scenario path on the right indicates that once the real device is connected to the switch, the Driver can request the appropriate handler from the provisioning site (this is in a sense similar to a plug-and-play device). The Server decodes the request and gets the handler object from the pool. This object is then installed in the Device handler slot, a placeholder that cannot do anything until a component gets installed. At this point, the installed device handler can prepare whatever operation is requested from a number of devices, which then get to perform the operation. The use of the handler can be repeated until no operations are required, and then the device(s) become idle.

Description of mobile behaviour

Dynamic responsibilities and pools can also be used to describe mobile behaviour that can be created, stored, retrieved, and installed in dynamic stubs. Figure 16/Z.152 illustrates this concept through an example that involves a telephone switch and a service creation environment. Similar to Figure 15/Z.152, the path on the left enables the creation and storage of new services (plug-ins) that are made available to the switch. The latter can dynamically request such service from the service creation environment, plug it in a dynamic stub, and initiate the execution of this service (in PerformService).

Service creation and execution map

The UCM notation thus proposes powerful constructs (dynamic stubs, dynamic responsibilities, pools, and slots) to capture and describe, in a concise way, complex scenarios that involve highly dynamic behaviour and architectures. This enables the representation of systems that involve agents and mobile code, two important features of the upcoming generation of distributed systems in general and telecommunications systems in particular.

Tool issues

TO BE DONE.

This informative appendix is intended to include lessons learned and issues observed while using a prototype tool supporting the Use Case Map (UCM) notation.

Currently, UCM support is provided by the UCM Navigator tool (UCMNav). UCMNav, developed at Carleton University. This tool is available at http://www.UseCaseMaps.org/tools/ucmnav/. More information on how to use the tool to create UCM models can be found on the UCM Web page: http://www.UseCaseMaps.org/. In particular, the paper  “Deriving Message Sequence Charts from Use Case Maps Scenario Specifications” (http://www.UseCaseMaps.org/pub/sdl01-miga.pdf) illustrates how to define and use scenario definitions in UCMNav in order to generate Message Sequence Charts automatically.

Bibliography

This section contains references to books, journal papers and conferences papers dealing with Use Case Maps (UCMs) and topics related to UCMs.

Amyot, D., Andrade, R., Logrippo, L., Sincennes, J., and Yi, Z. (1999) “Formal Methods for Mobility Standards”. In: IEEE 1999 Emerging Technology Symposium on Wireless Communications & Systems, Richardson, Texas, USA, April 1999. http://www.UseCaseMaps.org/pub/ets99.pdf

Amyot, D. and Andrade, R. (1999) “Description of Wireless Intelligent Network Services with Use Case Maps”. In: SBRC’99, 17º Simpósio Brasileiro de Redes de Computadores, Salvador, Brazil, May 1999, 418-433. http://www.UseCaseMaps.org/pub/sbrc99.pdf

Amyot, D., Buhr, R.J.A., Gray, T., and Logrippo, L. (1999) “Use Case Maps for the Capture and Validation of Distributed Systems Requirements”. In: RE'99, Fourth IEEE International Symposium on Requirements Engineering, Limerick, Ireland, June 1999, 44-53. http://www.UseCaseMaps.org/pub/re99.pdf

Amyot, D. and Logrippo, L. (2000) “Use Case Maps and Lotos for the Prototyping and Validation of a Mobile Group Call System”. In: Computer Communication, 23(12), 1135-1157. http://www.UseCaseMaps.org/pub/cc99.pdf

Amyot, D., Charfi, L., Gorse, N., Gray, T., Logrippo, L., Sincennes, J., Stepien, B., and Ware, T. (2000) “Feature description and feature interaction analysis with Use Case Maps and Lotos”. In: Sixth International Workshop on Feature Interactions in Telecommunications and Software Systems (FIW'00), Glasgow, Scotland, UK, May 2000. http://www.UseCaseMaps.org/pub/fiw00lotos.pdf

Amyot, D. and Mussbacher, G. (2000) “On the Extension of UML with Use Case Maps Concepts”. In: <<UML>>2000, 3rd International Conference on the Unified Modeling Language, York, UK, October 2000. http://www.UseCaseMaps.org/pub/uml2000.pdf

Amyot, D. (2000) “Use Case Maps as a Feature Description Language”. In: S. Gilmore and M. Ryan (Eds), Language Constructs for Designing Features. Springer-Verlag. http://www.UseCaseMaps.org/pub/fireworks2000.pdf

Amyot, D. and Eberlein, A. (2001) “An Evaluation of Scenario Notations for Telecommunication Systems Development”. In: 9th International Conference on Telecommunications Systems (ICTS'01), Dallas, USA, March 2001. http://www.UseCaseMaps.org/pub/icts01.pdf

Andrade, R. (2000) “Applying Use Case Maps and Formal Methods to the Development of Wireless Mobile ATM Networks”. In: Lfm2000, The Fifth NASA Langley Formal Methods Workshop, Williamsburg, Virginia, USA, June 2000. http://www.UseCaseMaps.org/pub/lfm2000.pdf

Andrade, R. and Logrippo, L. (2000) “Reusability at the Early Development Stages of the Mobile Wireless Communication Systems”. In: Proceedings of the 4th World Multiconference on Systemics, Cybernetics and Informatics (SCI 2000), Vol. VII, Computer Science and Engineering: Part I, Orlando, Florida, pp. 11-16, July 2000. http://www.UseCaseMaps.org/pub/sci2000.pdf

Andrade, R. (2001) Capture, Reuse, and Validation of Requirements and Analysis Patterns for Mobile Systems. Ph.D. thesis, SITE, University of Ottawa, Canada, Mai 2001. http://lotos.site.uottawa.ca/ftp/pub/Lotos/Theses/ra_phd.pdf

Bordeleau, F. and Buhr, R.J.A. (1997) “The UCM-ROOM Design Method: from Use Case Maps to Communicating State Machines”. In: Conference on the Engineering of Computer-Based Systems, Monterey, USA, March 1997. http://www.UseCaseMaps.org/pub/UCM-ROOM.pdf

Bordeleau, F. (1999) A Systematic and Traceable Progression from Scenario Models to Communicating Hierarchical Finite State Machines. Ph.D. thesis, School of Computer Science, Carleton University, Ottawa, Canada. http://www.UseCaseMaps.org/pub/fb_phdthesis.pdf

Bordeleau, F. and Cameron, D. (2000) “On the Relationship between Use Case Maps and Message Sequence Charts”. In: 2nd  Workshop of the SDL Forum Society on SDL and MSC (SAM2000), Grenoble, France, June 2000. http://www.UseCaseMaps.org/pub/sam2000.pdf

Buhr, R.J.A. and Casselman, R.S. (1996) Use Case Maps for Object-Oriented Systems, Prentice-Hall, USA. http://www.UseCaseMaps.org/pub/UCM_book95.pdf

Buhr, R.J.A. (1998) “Use Case Maps as Architectural Entities for Complex Systems”. In: IEEE Transactions on Software Engineering, Special Issue on Scenario Management. Vol. 24, No. 12, December 1998, 1131-1155. http://www.UseCaseMaps.org/pub/tse98final.pdf

Buhr, R.J.A., Amyot, D., Elammari, M., Quesnel, D., Gray, T., and Mankovski, S. (1998) “High Level, Multi-agent Prototypes from a Scenario-Path Notation: A Feature-Interaction Example”. In: H.S. Nwana and D.T. Ndumu (Eds), PAAM’98, Third Conference on Practical Application of Intelligent Agents and Multi-Agents, London, UK, March 1998, 277-295. http://www.UseCaseMaps.org/pub/4paam98.pdf

Buhr, R.J.A., Amyot, D., Elammari, M., Quesnel, D., Gray, T., and Mankovski, S. (1998) “Feature-Interaction Visualization and Resolution in an Agent Environment”. In: K. Kimbler and L. G. Bouma (Eds), Fifth International Workshop on Feature Interactions in Telecommunications and Software Systems (FIW'98), Lund, Sweden, September 1998. IOS Press, 135-149. http://www.UseCaseMaps.org/pub/fiw98.pdf

Buhr, R.J.A., Elammari, M., Gray, T., and Mankovski, S. (1998) “Applying Use Case Maps to Multi-agent Systems: A Feature Interaction Example”. In: Hawaii International Conference on System Sciences (HICSS’98), Hawaii, January 1998. http://www.useCaseMaps.org/pub/hiccs98.pdf

Buhr, R.J.A. (1999), “Understanding Macroscopic Behaviour Patterns in Object-Oriented Frameworks, with Use Case Maps”. In: Fayad, M.E., Schmidt, D.C., and Johnson, R.E. (eds) Building Application Frameworks: Object-Oriented Foundations of Framework Design. John Wiley & Sons. http://www.UseCaseMaps.org/pub/uoof.pdf

Elammari, M. and Lalonde, W. (1999) “An Agent-Oriented Methodology: High-Level and Intermediate Models”. In: Proc. of the 1st Int. Workshop on Agent-Oriented Information Systems (AOIS'99), Heidelberg, Germany, June 1999. http://www.UseCaseMaps.org/pub/aom-aois99.pdf

Gordijn, J. and van Vliet, J.C. (1999) “Integral Design of E-Commerce Systems: Aligning the Business with Software Architecture through Scenarios”. In: ICT-Architecture in the BeNeLux, 1999. http://www.UseCaseMaps.org/pub/ict99.pdf

Gordijn, J., de Bruin, H. and Akkermans, J.M. (2001) “Scenario Methods for Viewpoint Integration in e-Business Requirements Engineering”. In: 34th Annual Hawaii International Conference on System Sciences (HICSS'01), Hawaii, USA, January 2001. http://www.UseCaseMaps.org/pub/hicss34-01.pdf

Gorse, N. (2001) “The Feature Interaction Problem: Automatic Filtering of Incoherences & Generation of Validation Test Suites at the Design Stage”. M.Sc. thesis, SITE, University of Ottawa, Canada, 2001. http://www.UseCaseMaps.org/pub/ng-thesis.zip

Hassine, J. (2001) Feature Interaction Filtering and Detection with Use Case Maps and LOTOS, M.Sc. thesis, University of Ottawa, Canada, February 2001. http://lotos.site.uottawa.ca/ftp/pub/Lotos/Theses/jh_msc.pdf

Hodges, J. and Visser, J. (1999) “Accelerating Wireless Intelligent Network Standards Through Formal Techniques”. In: IEEE 1999 Vehicular Technology Conference (VTC’99), Houston (TX), USA. http://www.UseCaseMaps.org/pub/vtc99.pdf

Liu, L. and Yu, E. (2001) “From Requirements to Architectural Design — Using Goals and Scenarios”. In: From Software Requirements to Architectures Workshop (STRAW 2001), Toronto, Canada, May 2001. http://www.UseCaseMaps.org/pub/straw01.pdf

Miga, A. (1998) Application of Use Case Maps to System Design with Tool Support. M.Eng. thesis, Dept. of Systems and Computer Engineering, Carleton University, Ottawa, Canada. http://www.UseCaseMaps.org/pub/am_thesis.pdf

Miga, A., Amyot, D., Bordeleau, F., Cameron, C. and Woodside, M. (2001) “Deriving Message Sequence Charts from Use Case Maps Scenario Specifications”. In: Tenth SDL Forum (SDL'01), Copenhagen, Denmark, June 2001. http://www.UseCaseMaps.org/pub/sdl01-miga.pdf

Nakamura, M., Kikuno, T., Hassine, J., and Logrippo, L. (2000). “Feature Interaction Filtering with Use Case Maps at Requirements Stage”. In: Sixth International Workshop on Feature Interactions in Telecommunications and Software Systems (FIW'00), Glasgow, Scotland, UK, May 2000. http://www.UseCaseMaps.org/pub/fiw00filter.pdf

Sales, I. and Probert, R. (2000) “From High-Level Behaviour to High-Level Design: Use Case Maps to Specification and Description Language”. In: SBRC'2000, 18º Simpósio Brasileiro de Redes de Computadores, Belo Horizonte, Brazil. http://www.UseCaseMaps.org/pub/sbrc00.pdf

Scratchley, W.C. and Woodside, C.M. (1999) “Evaluating Concurrency Options in Software Specifications”. In: MASCOTS’99, Seventh International Symposium on Modelling, Analysis and Simulation of Computer and Telecommunication Systems, College Park, MD, USA, October 1999, 330-338. http://www.UseCaseMaps.org/pub/mascots99.pdf

Scratchley, W.C. (2000) Evaluation and Diagnosis of Concurrency Architectures. Ph.D. thesis, Dept. of Systems and Computer Engineering, Carleton University, Ottawa, Canada, June 2000.

Use Case Maps Web Page and UCM User Group (1999-). http://www.UseCaseMaps.org

Yi, Z. (2000) CNAP Specification and Validation: A Design Methodology Using LOTOS and UCM. M.Sc. thesis, SITE, University of Ottawa, Canada. http://lotos.site.uottawa.ca/ftp/pub/Lotos/Theses/zm_msc.pdf

UCM Change Request Form

| Please fill in the following details |
| --- |
| Character of change: |  error correction |  clarification |
|  |  simplification |  extension |
|  |  modification |  decommission |
| Short summary of change request |
| Short justification of the change request |
| Have you consulted other users |  yes |  no |
| Is this view shared in your organization |  yes |  no |
|  |  11-100 |  over 100 |
| How many users do you represent? | q 1-5 | q 6-10 |
|  | q 11-100 | q over 100 |
| Your name and address |

Please attach further sheets with details if necessary

URN (Z.150) Rapporteur, c/o ITU-T, Place des Nations, CH-1211, Geneva 20, Switzerland. Fax: +41 22 730 5853, e-mail: URN.rapporteur@itu.int